## Slide 1: Real Time Group
C for Embedded
Systems
bennyc@rt-ed.co.il

## Slide 2: דברי פתיחה
עם פתיחת מסלול הלימודים
צוות מכללת Real Time מאחל לכם חווית לימוד איכותית ופרודוקטיבית.
קורסי ההכשרה מקצועית מכוונים לנתב את הקריירה שלך למסלול שבו תוכל/י
להשתלב בתעשייה במקצוע שמעניין אותך ולמקסם את הידע בצורה אופטימאלית האפשרית.
תרגישו נוח לפנות אלינו בכל נושא.
בני כהן
מנכ"ל
Notes: Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.

## Slide 3: Index
Copyright @ 2007 Real Time College
3
Introduction 5
Variable And Constants 20
Expressions And Statements 42
Loops 60
Functions 71
Header Files 85
Arrays 89
Pointers 97
Strings 103
Dynamic Memory Allocations 116
Arguments to main 131
Pointer to Functions 134
Structures 137
Bitwise Operations 145
Big & Little Endian 151
Bit Fields & Unions 155
IO commands 166
the extern Keyword 179
Notes: 3
What do the <> mean?
Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.
Can your program have more than one .c file?
A ‘.c’ file is called a “module”. Many programs are composed of several ‘.c’ files and libraries that are ‘linked’ together during the compile process.

## Slide 4: Index
Copyright @ 2007 Real Time College
4
Static Variables 181
Linked Lists 185
Hash Tables 193
Sorting Methods 197
Notes: 4
What do the <> mean?
Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.
Can your program have more than one .c file?
A ‘.c’ file is called a “module”. Many programs are composed of several ‘.c’ files and libraries that are ‘linked’ together during the compile process.

## Slide 5
Introduction

## Slide 6: Introduction - Concepts of Embedded (Hardware)
Let us look at the concepts of Embedded programming through the eyes of a hardware developer. What do we need in order to make an embedded system work ?
Embedded System
CPU
Memory
Internal Bus
CPU
Memory
Peripherals
Internal Bus
Power Supply
Clocking Unit
Storage Unit
….
Peripherals

## Slide 7: Introduction - Concepts of Embedded (Programming)
Lets say I want to run a program in my embedded system.
Better yet, I created one, and I want to run it … where is the program located ?
Embedded System
CPU
Memory
Internal Bus
Peripherals
MyProg.c
Programming
MyProg.exe
Building The Program
MyProg
Process
Running
MyProg Files

## Slide 8: Introduction - Concepts of Embedded (Program In Mem)
Files will be located in the storage unit (HD, USB, Flash, CD/DVD etc..).
But a running program must run from memory ! Let’s look closer at the process.
Embedded System
CPU
Memory
Internal Bus
Peripherals
MyProg.C
MyProg.obj
MyProg.exe
MyProg
MyProg Process

## Slide 9: Introduction - Concepts of Embedded (Program In Mem)
Files will be located in the storage unit (HD, USB, Flash, CD/DVD etc..).
But a running program must run from memory ! Let’s look closer at the process.
Embedded System
CPU
Memory
Internal Bus
Peripherals
MyProg.C:
a text file, coded in ASCII or UNICODE
MyProg.obj
MyProg.exe:
Both are binary files, coded to work with the CPU
MyProg
MyProg Process
Data (Variables)
The Program has to remember data,
For example, Counters, Strings, Addresses, Objects
aka. Data / Stack / heap segments
Code (CPU Orders)
The binary orders that the cpu reads,
aka. Op-Codes.

## Slide 10: Introduction - Concepts of Embedded (Program In Mem)
MyProg Process
Lets assume I have created an application. A simple example of “Loading ..” menu would appear like this:
CPU
Internal Bus
Peripherals
Data (Variables)
Parameters for the Loading Window
Counter for the load percentage
String: “Loading ..”
Code (CPU Orders)
Fetch next file thread
Update counter thread
Memory
0x12ffa000
0x12ffb000
0x12ffc000
0x1000
0x1020
0x1030
0x1100
0x30fe0000
0x30ff0000

## Slide 11: Introduction - Concepts of Embedded (Program In Mem)
MyProg Process
The CPU Knows everyone by it’s address (memory and hardware). It also has special internal memory cells called CPU Registers. All the orders are executed within the CPU by those Registers
CPU
Internal Bus
Peripherals
Data (Variables)
Parameters for the Loading Window
Counter for the load percentage
String: “Loading ..”
Code (CPU Orders)
Fetch next file thread
Update counter thread
Memory
Rectangle Object for my “Loading …”window
String for “Loadin..”
‘L’
‘o’
‘a’
‘d’
‘i’
‘n’
‘g’
Loading Counter%
0x12ffa000
0x12ffb000
0x12ffc000
0x1000
0x1020
0x1030
0x1100
mov [0x12ffb000] R1
call update_counter
mov R1 [0x12ffb000]
Internal Registers:
IP = 0x30ff0000
R1
R2
R3
R4
.
.
.
.
45%
0x30fe0000
0x30ff0000

## Slide 12: Hello World
#include <stdio.h>
/* The simplest C Program */
int main(int argc, char **argv)
{
printf(“Hello World\n”);
return 0;
}
The main() function is always where your program starts running.
#include inserts another file. “.h” files are called “header” files. They contain stuff needed to interface to libraries and code in other “.c” files.
This is a comment. The compiler ignores this.
Prints out a message.
‘\n’ means “new line”.
Return ‘0’ from this function
What does the < > mean?
Can your program have more than one .c file?
Notes: What do the <> mean?
Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.
Can your program have more than one .c file?
A ‘.c’ file is called a “module”. Many programs are composed of several ‘.c’ files and libraries that are ‘linked’ together during the compile process.

## Slide 13: Hello World
The preprocessor runs before your compiler each time the compiler is invoked, Looking for lines beginning with pound symbol (#).
main() - Every C/C++ program has a main() function.
A function is a block of code that performs one or more actions.
Each time your program starts, main() is called automatically.
main(), like all functions, must state what kind of value it gets and returns.
If the return value type is void – function will not return any value at all
int – a value is returned
Notes: What do the <> mean?
Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.
Can your program have more than one .c file?
A ‘.c’ file is called a “module”. Many programs are composed of several ‘.c’ files and libraries that are ‘linked’ together during the compile process.

## Slide 14: the main() Function
#include <stdio.h>
/* The simplest C Program */
int main(int argc, char **argv)
{
printf(“Hello World\n”);
return 0;
}
Function Arguments
Return type, or void
Calling a Function: “printf()” is just another function, like main(). It’s defined for you in a “library”, a collection of functions you can call from your program.
Returning a value
main() is a Function. It’s only special because it always gets called first when you run the program. You can pass Arguments to a function and it can return a Value.
Notes: Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.

## Slide 15: Basic I\O Commands
In order to communicate with the outside world we need I\O functions.
scanf() – gets characters from keyboard
Example: read from keyboard into a variable called var1 in decimal mode
Scanf(“%d”,&var1)
printf() – writes characters to monitor
Example: write from a variable called var1 onto the screen in decimal mode
printf(“ variable is equal %d”, variable)
Notes: Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.

## Slide 16: Basic I\O Commands (2)
Copyright @ 2007 Real Time College
16
For example:
#include <stdio.h>
int main ()
{
int decimal; // uninitialized value
float pie=3.14; // initialized value to pie
printf(“please enter a decimal number: ”);
scanf(“%d”, &decimal);
printf(“the number you entered is: %d\n”, decimal);
printf(“but pie is closer to %f”, pie);
return 0;
}
my_program
Operating
System
Input
output
OUTPUT:
please enter a decimal number: 15
the number you entered is: 15
but pie is closer to 3.14
Notes: 16
Include directives use <x.h> (brackets) to indicate that the compiler should look in a “standard” place, such as /usr/include/…
They use “x.h” (double quotes) to indicate that it should look first in the current directory.

## Slide 17: Compiling and Linking
GNU cc (gcc) is the GNU project’s compiler suite. It compiles programs written in C, C++. gcc gives the programmer extensive control over the compilation process. The compilation process includes up to four stages:
Preprocessing
Compilation
Assembly
c\c++ src & hdr files
asm src & hdr files
Object files
Linking
Executable files
Archiving
Library files
17

## Slide 18: How does it work
File1.c
File2.c
File3.c
File1.i
File2.i
File3.i
File1.o
File2.o
File3.o
MyApp
Write down the action’s name
Write down the action’s name
Write down the action’s name

## Slide 19: The Pre-Processor
#include <stdio.h>
/* The simplest C Program */
int main(int argc, char **argv)
{
printf(“Hello World\n”);
return 0;
}
typedef unsigned long long int __dev_t;
typedef unsigned int __uid_t;
typedef unsigned int __gid_t;
typedef unsigned long int __ino_t;
Preprocessing
Compile
Compilation occurs in two steps:
“Preprocessing” and “Compiling”
In Preprocessing, source code is “expanded” into a larger form that is simpler for the compiler to understand. Any line that starts with ‘#’ is a line that is interpreted by the Preprocessor.
Include files are “pasted in” (#include)
Macros are “expanded” (#define)
Comments are stripped out ( /* */ , // )
Continued lines are joined ( \ )
Notes: Why preprocess? Having two phases to a process with different properties often helps to make a very flexible yet robust system. The underlying compiler is very simple and its behavior is easily understood. But because of that simplicity it can be hard to use. The preprocessor lets you “customize” the way your code “looks and feels” and avoid redunancy using a few simple facilities, without increasing the complexity of the underlying compiler. Macros can be used to make your code look clean and easy to understand. They can also be used for “evil”.
What are continued lines? Continued lines are lines that need to be very long. When the preprocessor encounters a ‘\’ (that is not inside a string), it will ignore the next character. If that character is a newline, then this “eats” the newline and joins the two lines into one. This is often used when defining macros with #define, because a macro must be all on one line. Be careful! If you have a space after a ‘\’, it will eat the space and will NOT join the lines.

## Slide 20: the Compiler
my_program
The compiler then converts the resulting source code into binary opcode the CPU can run directly
The binary file created is really series of Opcodes for the CPU to run
The Compiler has to be Architecture specific.
Compiling
And
Linking
An executable file
typedef unsigned long long int __dev_t;
typedef unsigned int __uid_t;
typedef unsigned int __gid_t;
typedef unsigned long int __ino_t;
Notes: Why preprocess? Having two phases to a process with different properties often helps to make a very flexible yet robust system. The underlying compiler is very simple and its behavior is easily understood. But because of that simplicity it can be hard to use. The preprocessor lets you “customize” the way your code “looks and feels” and avoid redunancy using a few simple facilities, without increasing the complexity of the underlying compiler. Macros can be used to make your code look clean and easy to understand. They can also be used for “evil”.
What are continued lines? Continued lines are lines that need to be very long. When the preprocessor encounters a ‘\’ (that is not inside a string), it will ignore the next character. If that character is a newline, then this “eats” the newline and joins the two lines into one. This is often used when defining macros with #define, because a macro must be all on one line. Be careful! If you have a space after a ‘\’, it will eat the space and will NOT join the lines.

## Slide 21
Variables And Constants

## Slide 22
A variable is a place to store information,
its located in your computer's memory (you can read or write to it).
The computer's memory can be viewed as a series of slots (one Byte each), Every Byte has an address.
Declaring a Variable - reserves one or more Bytes.
The variable's name (myVar in this case) is a label on one of these cubbyholes, so that you access it easily without knowing its actual memory address.
For example, myVar starts at
memory address 0xFF08 and its size can take up one or more memory addresses.
Addr | Value
0xFF00 | 
0xFF01 | 
0xFF02 | 
0xFF03 | 
0xFF04 | (72)
0xFF05 | (101)
0xFF06 | ‘l’ (108)
0xFF07 | ‘l’ (108)
0xFF08 | (111)
0xFF09 | ‘\n’ (10)
0xFF0A | ‘\0’ (0)
myVar
Variables (1)

## Slide 23
char x;
char y=‘e’, y1, y2;
Type (for example: char. occupies a single byte)
Additional attributes can be set. Keep on reading ….
Name
What names are legal?
Initial value
Initial value of x is undefined
The compiler puts them somewhere in memory.
Addr | Value
0xFF00 | 
0xFF01 | 
0xFF02 | 
0xFF03 | 
0xFF04 | ‘e’ (101)
0xFF05 | (72)
0xFF06 | ‘l’ (108)
0xFF07 | ‘l’ (108)
0xFF08 | (111)
0xFF09 | ‘\n’ (10)
0xFF0A | ‘\0’ (0)
Variables (2)
A Variable names a place in memory where you store a Value of a certain Type.
You define a variable by giving it a name and specifying the type, and optionally an initial value (example below).
Multiple definition can be done by using a comma seperator (,).
Notes: Symbol table: The “Symbol Table” is the mapping from symbol to address. You can extract this from a compiled program (if debugging is enabled aqt compile time with –g) using the nm utility.
Declaration and definition mean slightly different things in C. Declaration is mapping a name to a type, but not to a memory location. Definition maps a name and type to a memory location (which could be the body of a function). Definitions can assign an initial value. Declarations can point to something that never actually gets defined, or is defined in a library external to your program.
What names are legal? Symbols in C (function and variable names) must start with an alphabetic character or ‘_’. They may contain numeric digits as well but cannot start with a digit. Common naming strategies are ‘CamelCase’, ‘lowerUpper’, and ‘under_bar’. Some people use complicated schemes but I prefer under_bar.
extern, static, and const are modifiers of variable declarations. ‘extern’ means the variable being declared is defined elsewhere in some other program module (.c file). ‘static’ means that the variable cannot be accessed outside of the current scope. ‘const’ means the variable’s value cannot be changed (directly).

## Slide 24
When defining a new variable, specifying the Variable Type (char \ int \ float etc..) is mandatory! this tells the compiler the amount of memory to allocate for this variable from RAM.
we can also tell the compiler the variables Initial Value (optional).
char myVariable = 111;
NOTE: RAM is Random Access Memory.
When a program runs, it is loaded into
RAM from the disk,
All variables are also created in RAM.
(Variables are not created in FLASH)
myVariable
What more attributes are there for variables ?
Variables (3)
Addr | Value
0xFF00 | 
0xFF01 | 
0xFF02 | 
0xFF03 | 
0xFF04 | 
0xFF05 | (111)
0xFF06 | 
0xFF07 | 
Lst0302.c
Notes: What’s 72? ASCII is the coding scheme that maps bytes to characters. Type ‘man ascii’ at the shell to get a listing of the mapping.
Not always… Types such as int vary in size depending on the architecture. On a 32 bit or 64 bit platform, ints are 4 bytes (32 bits). On an 8 or 16 bit platform, an int is 2 bytes (16 bits). To be safe, it’s best to specify types exactly e.g. int32_t, int16_t., int8_t. Defined in #include <inttypes.h>
Signed? Signedness is a common source of problems in C. It’s always clearest to specify signness explicitly (and size) using the [u]int[8,16,32]_t types. Signedness can introduce surprises when casting types because of “sign extension”. For example, char is signed (although it’s normally used as unsigned 0-255). If you cast char to int, it will be a signed integer and the sign will be extended. If you then cast that to unsigned, it turns a small negative number into an enormous int value (high bit set). That is, (uint32_t)(int)(char)(128) == 4294967168 (not 128!)
One easy solution to this is to always use uint8_t rather than char for byte streams.

## Slide 25
The variable name can be any combination of letters, numbers, and also the char ‘_’, but cannot contain white spaces. The first letter of a variable cannot be numeric.
The name should tell you what the variable is used for; using good names makes it easier to understand the flow of your program,
You cannot use Keywords as variables (if, while…)
It is a common convention to use a lower case first character name for a regular variable. Each company / community has its own standards of coding style.
e.g: int myAge, hisAge, ageing;
Variable names
NOTE: C is case-sensitive -
uppercase and lowercase letters are considered to be different.
A variable named age is different from Age, which is different from AGE.

## Slide 26: the table shows the variable type, how much room it takes in memory. The values that can be stored are determined by the size of the variable types.
Variable types can be divided into
integer
floating-point
character
Type | Size in bytes
int (Signed / unsigned doesn’t change size) | 4 bytes (arch dependent)
short | 2 bytes
long | 4 bytes
long long | 8 bytes
float | 4 bytes
double | 8 bytes
long double | 16 bytes
char | 1 bytes
NOTE: Variable sizes might change
between architectures.
Variable Types
Notes: What’s 72? ASCII is the coding scheme that maps bytes to characters. Type ‘man ascii’ at the shell to get a listing of the mapping.
Not always… Types such as int vary in size depending on the architecture. On a 32 bit or 64 bit platform, ints are 4 bytes (32 bits). On an 8 or 16 bit platform, an int is 2 bytes (16 bits). To be safe, it’s best to specify types exactly e.g. int32_t, int16_t., int8_t. Defined in #include <inttypes.h>
Signed? Signedness is a common source of problems in C. It’s always clearest to specify signness explicitly (and size) using the [u]int[8,16,32]_t types. Signedness can introduce surprises when casting types because of “sign extension”. For example, char is signed (although it’s normally used as unsigned 0-255). If you cast char to int, it will be a signed integer and the sign will be extended. If you then cast that to unsigned, it turns a small negative number into an enormous int value (high bit set). That is, (uint32_t)(int)(char)(128) == 4294967168 (not 128!)
One easy solution to this is to always use uint8_t rather than char for byte streams.

## Slide 27
This keyword function is provided by your compiler, and it tells you the size of the object you pass in as a parameter (in bytes).
Example:
char a3; short a2; int a1;
1 = sizeof(a3) = sizeof(char )
2 = sizeof(a2) = sizeof(short )
4 = sizeof(a1) = sizeof(int)
Lst0201.cxx
sizeof()

## Slide 28
Coding Style
main () { <tab> int myWidth; <tab> int myLength; .. int itsArea;
itsArea=myWidth*myLength; }
main () { <tab> int my_width; <tab> int my_length; .. int its_area;
its_area=my_width*my_length; }
NOTE :
There are two popular conventions: myCar or my_car.
The first latter form is called camel-notation, because the capitalization looks something like a camel's hump.
Some people find the underscore character (my_car) to be easier to read.

## Slide 29
Signed / Unsigned (1)
integer types come in two varieties:
signed / unsigned
Integers (short and long) without the word "unsigned" are assumed to be signed.
Signed integers - are either negative or positive: (short e.g. -32,768 to 32,767).
Unsigned integers - are always positive: (short e.g. 0 to 65,535)
you have the same number of bytes for both signed and unsigned integers, so the largest number you can store in an unsigned integer is twice as big as the largest positive number you can store in a signed integer.
Notes: What’s 72? ASCII is the coding scheme that maps bytes to characters. Type ‘man ascii’ at the shell to get a listing of the mapping.
Not always… Types such as int vary in size depending on the architecture. On a 32 bit or 64 bit platform, ints are 4 bytes (32 bits). On an 8 or 16 bit platform, an int is 2 bytes (16 bits). To be safe, it’s best to specify types exactly e.g. int32_t, int16_t., int8_t. Defined in #include <inttypes.h>
Signed? Signedness is a common source of problems in C. It’s always clearest to specify signness explicitly (and size) using the [u]int[8,16,32]_t types. Signedness can introduce surprises when casting types because of “sign extension”. For example, char is signed (although it’s normally used as unsigned 0-255). If you cast char to int, it will be a signed integer and the sign will be extended. If you then cast that to unsigned, it turns a small negative number into an enormous int value (high bit set). That is, (uint32_t)(int)(char)(128) == 4294967168 (not 128!)
One easy solution to this is to always use uint8_t rather than char for byte streams.

## Slide 30
signed char ch = 130; // same as ch = -126;
Signed / Unsigned (2)
unsigned char ch = 130; // same as ch = -126
1
1
0
0
0
0
0
0
1
1
0
0
0
0
0
0
If not specified, the type will be signed.
For example char ch = 255 sets ch with the value of 0xFF (= -1)
Notes: What’s 72? ASCII is the coding scheme that maps bytes to characters. Type ‘man ascii’ at the shell to get a listing of the mapping.
Not always… Types such as int vary in size depending on the architecture. On a 32 bit or 64 bit platform, ints are 4 bytes (32 bits). On an 8 or 16 bit platform, an int is 2 bytes (16 bits). To be safe, it’s best to specify types exactly e.g. int32_t, int16_t., int8_t. Defined in #include <inttypes.h>
Signed? Signedness is a common source of problems in C. It’s always clearest to specify signness explicitly (and size) using the [u]int[8,16,32]_t types. Signedness can introduce surprises when casting types because of “sign extension”. For example, char is signed (although it’s normally used as unsigned 0-255). If you cast char to int, it will be a signed integer and the sign will be extended. If you then cast that to unsigned, it turns a small negative number into an enormous int value (high bit set). That is, (uint32_t)(int)(char)(128) == 4294967168 (not 128!)
One easy solution to this is to always use uint8_t rather than char for byte streams.

## Slide 31
Signed / Unsigned (3)
0 0000 0000
2 0000 0010
-2 1111 1110
-1 1111 1111
3 0000 0011
And so on…
126 0111 1110
127 0111 1111
-128 1000 0000
-127 1000 0001
-126 1000 0010
1 0000 0001
And so on…
-3 1111 1101
0 0000 0000
2 0000 0010
254 1111 1110
255 1111 1111
3 0000 0011
And so on…
126 0111 1110
127 0111 1111
128 1000 0000
129 1000 0001
130 1000 0010
1 0000 0001
And so on…
253 1111 1101
0
127
-128
255
Singed
Unsigned
40
Singed
Unsigned
200
-56
For example:
3 - 3 = 0
0000 0011 equals 3
1111 1101 equals -3
---------------
0000 0000
Sign bit on makes a value negative
Positive signed = Unsigned values
Adding X and –X in binary results in 0
Sign bit on makes no difference
Cannot save a negative number
The highest number will be -1
For example:
char ch = -1;
ch  1111 1111
Which is 255
Try it in short/long int

## Slide 32
If there is any chance that the value you'll want to put into your variable will be too big for its type, use a larger type.
When an unsigned integer reaches its maximum value, it wraps around and starts over, much as a car’s speedometer might.
Example:
unsigned short int smallNumber;
smallNumber = 65535;//0xffff
smallNumber++
Short \ Long
Lst0204.cxx and Lst0205.cxx

## Slide 33
It can become tedious, repetitious, and, most important, error-prone to keep writing unsigned short int.
C/C++ enables you to create an alias for this phrase by using the keyword typedef, which stands for type definition.
typedef is used by writing the keyword typedef, followed by the existing type and then the new name.
It is considered a better practice to distinguish types from variables by naming them with a capital letter as a first letter, or add _t at the end of a new type. Also common types are: U8 / U16 / U32 or uint / ushort / ulong or uint8 / uint16 / uint32 etc…
Example
typedef unsigned short int U16; //typedef defined
U16 width = 5;
Lst0203.c
typedef

## Slide 34
When you put a character, for example, 'a', into a char variable, what is really there is just a number between 0 and 255.
The compiler knows, how to translate back and forth between characters.
The value/letter relationship is mapped according to a known char-map called ASCII table. for example lowercase "a" is assigned the value 97 decimal.
Important - there is a big difference between the value 5 and the character ‘5’. The letter is actually valued at 53, much as the letter 'a' is valued at 97.
The compiler recognizes some special characters for formatting. You put these into your code by typing the backslash (called the escape character), followed by the character.
Lst0206.cxx
The Escape Characters.
\n new line
\t tab
\b backspace
\" double quote
\' single quote
\? question mark
\\ backslash
Characters and Numbers
See the full map at Lesson1 ascifull

## Slide 35
Copyright @ 2007 Real Time College
35
C/C++ can help you convert between different types, this is called casting.
There are two forms of casting. Implicit and Explicit.
Implicit: the type is converted according to the receiver’s variable type.
// Implicit example:
int a = 5.25; // a equals 5 after init.
Explicit: the type is specifically converted to a different type.
// Explicit example:
float f = (float) 5.25; // f equals 5.25 after init.
/* floating point’s default type (like 5.25) is double. */
Syntax: (casting type) <expression>
Casting

## Slide 36
I/O Commands printf/scanf formats
Copyright @ 2007 Real Time College
36
Unsigned hexadecimal value / (type *), %p used for pointers.
%x , %X , %p
Unsigned decimal integer (int)
%u
String of text (char *)
%s
Unsigned octal (base 8) integer (int)
%o
Signed decimal integer (int)
%i (same as %d)
Signed value in %e or %f format, whichever is shorter
%g , %G
Signed floating-point value (float)
%f , %F
Signed floating-point value in E notation (example: 10000 -> 1e04)
%e , %E
Signed decimal integer (int)
%d
Single character (char)
%c
Displays Argument (Variable's Contents) As
Conversion Character
printf and scanf uses the following format for it’s printable text:
%[parameter][flags][width][.precision][length]type
Most commonly used are: %c, %d, %f, %s, %x, %p
%[Capital letters] prints the hex characters in Upper-Case

## Slide 37
I/O Commands printf/scanf formats
Copyright @ 2007 Real Time College
37
printf is able to print text and variables, or just one of the two. As for scanf though, it is only able to scan for variables.
Using width will cause the print function to allocate in advance space for the printed variable.
Using precision will cause the print function to show X characters of floating points.
%[parameter][flags][width][.precision][length]type
For example:
printf(“num1: %3d\n”,1);
printf(“num2: %3d\n”,12);
printf(“num3: %3d\n”,123);
printf(“10/3 = %f, pretty accurate\n”, 10/3.);
printf(“10/3 = %6.2f , easier to read\n”, 10/3.);
OUTPUT
num1: 1
num2: 12
num3: 123
10/3 = 3.33333333, pretty accurate
10/3 = 3.33, easier to read

## Slide 38: Table of printf format specifiers:
%hhu | unsigned char | %hhd | char
%hu | unsigned short int | %hd | short int
%u | unsigned int | %d | int
%lu | unsigned long int | %ld | long int
%llu | unsigned long long int | %lld | long long int
%e | float (scientific) | %f | float (normal display)
%le | double (scientific) | %lf | double (normal display)
%Le | long double (scientific) | %Lf | long double (normal display)
%[parameter][flags][width][.precision][length]type

## Slide 39
Like variables, constants are data storage locations. Unlike variables, constants don't change.
You must initialize a constant when you create it, and you cannot assign a new value to it later. There are two ways to declare constants in C/C++. The old, traditional, and obsolete way is with a preprocessor directive, #define.
#define studentsPerClass 15
Every time the preprocessor sees the word studentsPerClass, it puts in the text 15. This type of constant is not a variable, and does not have space in memory. It is simply an expression of a macro.
there is a new, much better way to define constants in C/C++:
const int studentsPerClass = 15;
This method has several advantages in making your code easier to maintain and in preventing bugs. The biggest difference is that this constant has a type, and the compiler can enforce that it is used according to its type.
Constants

## Slide 40
Enables to create new types and to define variables of those types whose values are restricted to a set of possible values.
For example: declare COLOR to be an enumeration, and that there are five values for COLOR: RED, BLUE, GREEN, WHITE, and BLACK.
enum COLOR { RED, BLUE, GREEN, WHITE, BLACK };
1. Makes COLOR the name of an enumeration, that is, a new type. 2. Makes RED a symbolic constant with the value 0, BLUE a symbolic constant with the value 1, GREEN equals 2, and so forth.
It is possible to initialized the constants with a particular value, however, and those that are not initialized will count upward from the ones before them.
enum Color { RED=100, BLUE, GREEN=500, WHITE,BLACK=700 };
RED will have the value 100; BLUE =101; GREEN= 500; WHITE = 501; and BLACK=700.
Enumerated Constants
Lst0207.c and
Lst0208.c

## Slide 41
After creating the type, using it (aka. Defining a variable in the enum’s type) will have either one of the following syntax:
1.
enum COLOR { RED, BLUE, GREEN, WHITE, BLACK };
enum COLOR screen_background = BLUE;
2.
enum COLOR { RED, BLUE, GREEN, WHITE, BLACK }
clr_background = RED, clr_text=GREEN, clr_window;
clr_window = WHITE;
This however can be shorten using typedef:
typedef enum Color { RED, BLUE, GREEN, WHITE,BLACK } Color_t;
Color_t clr_bground = RED, clr_text=GREEN, clr_window;
clr_window = WHITE;
Enumerated Constants (2)
Lst0207.c and
Lst0208.c

## Slide 42
This subject will be deeply covered later on, but just as an intro, you can group several variables into one structured object using the keyword struct. The syntax is exactly as enum. Again, for more information skip ahead for the structs chapter.
1.
struct Point { int x, int y };
struct Point my_point;
my_point.x = 5;
2.
struct Point { int x, int y } my_point;
my_point.y = 5;
Shorten using typedef:
typedef struct Point { int x, int y } Point_t;
Point_t my_point;
my_point.x = 5;
Creating a structured object

## Slide 43
Expressions
And
Statements

## Slide 44
Anything that evaluates to a value is an expression in C.
An expression is said to return a value.
For example
3+2 returns the value 5 and so it is an expression.
x = a + b;
This example is evaluated in the following order:
1.Add a to b.
2. Assign the result of the expression a + b to x.
y = x;
3.Assign the result of the assignment expression x (= a + b) to y.
4.1 - expressions
Expressions

## Slide 45
An operator is a symbol that causes the compiler to take an action. Operators act on operands. The operators listed by their categories as follows:
Arithmetic operators + - * / % ++ --
Comparison operators/relational operators == != <= >= < >
Logical operators && || !
Bitwise operators & | ~ ^ << >>
Assignment operators = [Arithmetic/Bitwise]=
Member and pointer operators [] & * -> .
Special operators ?: sizeof() (type)casting
Operators (1)

## Slide 46
As we mentioned, there are several different categories of operators. Two of these categories are
    Assignment operators.
    Arithmetical operators.
The assignment operator (=) causes the operand on the left side of the assignment operator to have its value changed to the value on the right side of the assignment operator. Constants are r-values. They cannot be l-values. you can write
x = 35; // ok
but you can't legally write
35 = x; // error, not an lvalue!
Operators (2)

## Slide 47
There are five mathematical operators: addition (+),
subtraction (-),
multiplication (*),
division (/),
modulus (%).
** 4.2. subtraction and overflow.
x += y assign (x+y) to x => x=x+y
x -= y assign (x-y) to x=> x=x-y
x *= y assign (x*y) to x => x=x*y
x /= y assign (x/y) to x => x=x/y
x %= y assign (x%y) to x => x=x%y
Shortcuts:
Operators (3)

## Slide 48
Integer division is different from everyday division. When you divide 21 by 4, the result is a real number (a number with a fraction).
Integers don't have fractions, and so the "remainder" is lopped off. The answer is therefore 5. To get the remainder, you take 21 modulus 4 (21 % 4) and the result is 1.
The modulus operator tells you the remainder after an integer division.
Beware of division:
If second argument is integer, the
result will be integer (rounded):
5 / 10  0 whereas 5 / 10.0  0.5
Division by 0 will cause a FPE
Integer Division and Modulus

## Slide 49
In C, increasing a value by 1 is called incrementing, and decreasing by 1 is called decrementing. There are special operators to perform these actions.
The increment operator (++) increases the value of the variable by 1, and the decrement operator (--) decreases it by 1
var++; var = var + 1; var += 1; //all the same
Var--; var = var - 1; var -= 1;
The rules of precedence are clearly defined but often difficult to remember or non-intuitive.
When in doubt, add parentheses to make it explicit.
Increment and Decrement

## Slide 50
Both the increment operator (++) and the decrement operator(--) come in two varieties: prefix and postfix.
Prefix: you have told the compiler to increment x (making it 5+1= 6) and then fetch that value and assign it to a.(x=x+1 and then a=x)
int a = ++x;
Postfix: fetch the value of x and assign it to a, then inc x . (a=x and then x=x+1)
Note the difference between ++x and x++:
**4.4. prefix and postfix.
Prefix and Postfix
int x=5;
int y;
y = ++x;
/* x == 6, y == 6 */
int x=5;
int y;
y = x++;
/* x == 6, y == 5 */

## Slide 51
Logical OR and AND operators are represented by:
|| = OR, && = AND. It will be discussed shortly.
In C, zero is considered false, and all other values are considered true, although true is usually represented by 1. If an expression equal to zero, it is false. If it is non zero, it is true.
Comparison Operators
The relational operators are used to determine whether two numbers are equal, or if one is greater or less than the other.
Every relational statement evaluates to either: 1 (TRUE) or 0 (FALSE).
Example: int x=4;
(x < 5)  (4 < 5)  1 <true>
(x < 4)  (4 < 4)  0 <false>
((x < 5) || (x < 4))  (<true> || (x < 4))  <true>
Equals ==
Not Equals !=
Greater >
Greater >= or Equal
Less <
Less <= or Equal

## Slide 52
The if Statement
The if statement enables you to test for a condition (such as whether two variables are equal) and branch to different parts of your code, depending on the result.
if (expression)
statement;
if (bigNumber > smallNumber) { statement1; statement2; statement3; }
**4.5. branching based on relational operators.
== equal to
< less than
<= less than or equal
> greater than
>= greater than or equal
!= not equal
&& logical and
|| logical or
! logical not

## Slide 53
The else keyword
Often your program will want to take one branch if your condition is true, another if it is false.
if (expression) { statements; }
else { statements; }
**4.6 the else keyword.
WARNING: Many C/C++ programmers confuse the assignment operator (=) with the equals operator (==). This can create a nasty bug in your program.

## Slide 54
Advanced if Statements
**4.6. A complex, nested if statement.
**4.7. how braces help clarify which else statement goes with which if statement.
**4.8. the proper use of braces with an if statement
if (expression1) { if (expression2) { statement1;
} else { statement2;
}
} else { statements; }

## Slide 55
else if Statements
if (expression1) {
statement1;
} else if (expression2) { statement2;
}
else if (expression3)
...
else { statement; }

## Slide 56
Logical Operators
A program might need to determine that couple of conditions are true, or that some other condition is true, in order to take an action.
Imagine a sophisticated alarm system that has this logic: "If the door alarm sounds AND it is after six p.m. AND it is NOT a holiday, OR if it is a weekend, then call the police." C/C++'s three logical operators are used to make this kind of evaluation.
Bitwise operators:
& - bitwise and
| - bitwise or
^ - bitwise xor
~ - bitwise not
<< - shift left
>> - shift right
Conditions usage ..
&& - logical and
|| - logical or
! - logical not

## Slide 57
A logical AND statement evaluates two expressions, and if both expressions are true, the logical AND statement is true .
If it is true that you are hungry, AND it is true that you have money, THEN it is true that you can buy lunch. Thus,
if ( (x == 5) && (y == 5) )
would evaluate TRUE if both x and y are equal to 5, and it would evaluate FALSE if either one is not equal to 5.
Note that both sides must be true for the entire expression to be true.
Note that the logical AND is two && symbols, A single & symbol is a different operator.
Don’t confuse & and &&..
1 & 2  0 whereas 1 && 2  <true>
Logical AND

## Slide 58
A logical OR statement evaluates two expressions. If either one is true, the expression is true.
If you have money OR you have a credit card, you can pay the bill. You don't need both money and a credit card; you need only one, although having both would be fine as well.
Thus,
if ( (x == 5) || (y == 5) )
evaluates TRUE if either x or y is equal to 5, or if both are.
Note that the logical OR is two || symbols. A single | symbol is a different operator,
Don’t confuse | and ||..
1 | 2  3 whereas 1 || 2  <true>
Logical OR

## Slide 59
Logical NOT
A logical NOT statement evaluates true if the expression being tested is false. Again, if the expression being tested is false, the value of the test is TRUE! Thus
if ( !(x == 5) )
is true only if x is not equal to 5. This is exactly the same as writing
if (x != 5)
NOTE: It is often a good idea to use extra parentheses to clarify what you want to group. Remember, the goal is to write programs that work and that are easy to read and understand.
Don’t confuse = and == The compiler might not warn.

## Slide 60
Ternary operator (if statement shortcut)
The if statement could be shortened to an if expression using the ternary operator – ‘?’. Consider this as an if expression.
if (expression) // condition
statement; // if true
else
statement; // if false
Syntax:
(expression-condition)?(statement-if-true):(statement-if-false)
Example:
char a=‘a’, A=‘A’, bigger=0; // a = ‘a’ (97), A = ‘A’ (65), bigger = 0
bigger = (a>A)?(a):(A); // bigger  ‘a’ (97)

## Slide 61
The switch Statement
you know how to write if and if/else statements. These can become quite confusing when nested too deeply, C offers an alternative. Unlike if, which evaluates one value, switch statements allow you to branch on any of a number of different values.
The general form of the switch statement is:
switch (expression) { case valueOne: statement; break;
case valueTwo: statement; break;
....
case valueN: statement; break;
default: statement; }
** 4.9. the switch statement.
**4.9. switch case in a forever loop.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 62
Loops

## Slide 63
Looping
Some programs need to repeatedly act on the same data. This is called iteration. Iteration means doing the same thing again and again. The principal method of iteration is the loop.
The type of loops used are:
While \ Do - While loops
For loops
Goto - obsolete
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 64
while Loops
A while loop causes your program to repeat a sequence of statements as long as the starting condition remains true.
The syntax for the while statement is as follows:
while ( condition )
{
statement;
statement; }
When condition evaluates to TRUE (1), statement is executed, and then condition is tested again. This continues until condition tests FALSE, at which time the while loop terminates and execution continues on the first line below statement.
**6.2. while loops.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 65
Complicated while Statements
The condition tested by a while loop can be as complex as any legal C/C++ expression. This can include expressions produced using the logical && (AND), || (OR), and ! (NOT) operators.
**6.3. Complex while loops.
while ( (i<MAX && strlen(s)<=10) || !(kbhit == 1 && key==ESC ) )
{
.....
}
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 66
The break Statement
break; causes the immediate end of a while or for loop. Execution jumps to the closing brace.
Example
while (condition)
{
if (condition2) { statements; break; }
statements; // will not be executed!!!
}
[statements];
**6.4. break and continue.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 67
The continue Statement
continue; causes end of a single iteration in while or for loop.
Execution jumps to the condition of the loop.
Example
while (condition)
{
if (condition2) { statements; continue; }
statements; // will not be executed!!!
}
**6.4. break and continue.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 68
The do...while Statement
The do...while loop executes the body of the loop before its condition is tested and ensures that the body always executes at least one time.
The syntax for the do...while statement is as follows:
do {
Statements
} while (condition);
statement is executed, and then condition is evaluated. If condition is TRUE, the loop is repeated; otherwise, the loop ends.
The statements and conditions are otherwise identical to the while loop.
**6.7. Demonstrates do...while loop.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 69
the for loop
for statements are powerful and flexible. includes three statements (initialization, condition, and action).
a for loop works in the following sequence:
1. Performs the operations in the initialization.
2. Evaluates the condition.
3. If the condition is TRUE, executes the statement(s) within the loop.
4. Do the action, and go to operation number 2
for (init; condition; action )
{
statement;
statement;
}
**6.9. the for loop.
1
2
3
4
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 70
Advanced for Loops
After each time through, the loop repeats steps 2 and 3 of the previous page.
Multiple Initialization and Increments, It is not uncommon to initialize more than one variable, to test a compound logical expression, and to execute more than one statement.
The initialization and the action may be replaced by multiple C statements, each separated by a comma.
**6.10. multiple statements in for loops.
**6.11. Null statements in for loops.
**6.12. empty for loop statement.
for (x=0, y=0; x<MAX_X && y<MAX_Y; x++, y++)
{
statement;
statement;
}
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 71
float pow(float x, uint exp)
{ float result=1.0;
int i;
for (i=0; (i < exp); i++) {
result = result * x;
}
return result;
}
int main(int argc, char **argv)
{
float p;
p = pow(10.0, 5);
printf(“p = %f\n”, p);
return 0;
}
float pow(float x, uint exp)
{ float result=1.0;
int i;
i=0;
while (i < exp) {
result = result * x;
i++;
}
return result;
}
int main(int argc, char **argv)
{
float p;
p = pow(10.0, 5);
printf(“p = %f\n”, p);
return 0;
}
The “for” and while”
loops differences.

## Slide 72
Nested Loops
**6.14. nested for loops.
Note:
many C\C++ programmers use the
letters i and j as counting
variables.
Loops may be nested, with one loop sitting in the body of another. The inner loop will be executed in full for every execution of the outer loop.
for (i=0; i<MAX_I; i++)
  for (j=0; j<MAX_J; j++)
  {
statement;
...
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 73
Functions
And
Headers

## Slide 74
A subprogram that acts on data and returns a value.
Every C\C++ program has at least one function, main(). When your program starts, main() is called automatically.
main()might call other functions, some of which might call still others.
Each function has its own name, and when that name is encountered, the execution of the program branches to the body of that function. When the function returns, execution resumes on the next line of the calling function.
Each function should carry out a single, easily understood task. If your functions start getting large,
look for places where you can divide them into component tasks.
Symbol | Addr | Value
Func_1 | 0xffb0 | push r0
 | 0xffb1 | push r1
 | 0xffb2 | mov r2, r0
 | 0xffb3 | inc r1
 | 0xffb4 | add r2, 4
 | 0xffb5 | call Func_2
 | 0xffb6 | pop r1
 | 0xffb7 | pop r0
 | 0xffb8 | ret
Func_2 | 0xffb9 | push r0
 | 0xffba | pop r0
 | 0xffbb | ret
What Is a Function?
1
2
3

## Slide 75
A function can have any number of parameters, in any type we choose, or none at all.
A function can have a return value (one only) of any type, or none (void).
We can view a function as a black box, in which we put our raw materials and get the final value (if there should be one) in return. For example:
void clear_screen();
no parameters, no return value
void set_background_color(Color rgb);
parameter color, no return value
Color get_background_color();
no parameters, returns the color
Color get_pixel_color(int x, int y);
two parameters, returns the color
What Is a Function? (cont’d)
clear_screen
set_background_color
get_background_color
get_pixel_color
rgb
x
y

## Slide 76
Using functions in your program requires that you :
  declare the function first
  define the function later.
The declaration tells the compiler the name, return type, and parameters of the function. The declaration of a function is called its prototype.
The definition tells the compiler how the function works (implementation).
Function Prototype Syntax:
return_type function_name ( [type [parameterName]]...);
Function Definition Syntax
return_type function_name ( [type parameterName]...)
{
statements;
}
**5.1. function declaration, definition and implementation.
Declaring and Defining Functions

## Slide 77: Func’s Example:
#include <stdio.h>
// declaration (aka interface / prototype)
int reverse_int(int num);
int get_right_digit(int num, int pos);
int get_left_digit(int num, int pos);
int main()
{
int num, rev_num;
int sec_right_digit, sec_left_digit;
printf(“please enter a number: “);
scanf(“%d”, &num)
rev_num = reverse_int(num);
sec_right_digit = get_right_digit(num, 2);
sec_left_digit = get_left_digit(num, 2);
return 0;
}
// definition (aka implementation)
int reverse_int(int num)
{
int rev = 0;
while (rev)
……
return rev;
}
int get_right_digit(int num, int pos)
{
int digit = 0;
while (--pos)
……
return digit;
}
int get_left_digit(int num, int pos)
{
return get_right_digit(reverse_int(num, pos);
}

## Slide 78
Usually when the code gets too long, it is recommended to divide it to multiple files.
For example, we have created a chess program, the program includes:
Set of objects and their rules, such as the board, the pieces, and their functions.
Printing functions, IO and GUI modules (mouse and keyboard handlers, screen etc.
A special object which contains a list of moves done by the players
Computer side algorithms …
and so on … it is recommended to set the modules in the following way:
Modular usage of functions
#include “io.h”
#include “gui.h”
#include ….
void func1();
void func2(..);
int main()
{
…
// declerations
int keypress(..);
int mousein(..);
..
// implementations
#include “io.h”
int keyperss(..)
{
…
}
int mousein(..)
{
…
Main.c
io.h
// declerations
int print(..);
int clear(..);
..
// implementations
#include “gui.h”
int print(..)
{
…
}
int clear(..)
{
…
io.c
gui.h
gui.c

## Slide 79
Interface Versus Implementation
Each function that you declare must have an implementation.
Usually the decelerations are stored in a header file - *.h (c++ uses *.hpp)
the implementations are in stored in a source file - *.c (c++ uses *.cpp)
You can think of the declarations as an interface to your functions - like a manual of how to use your code (more specifically - your functions, macros and data types).
The header file tells what data your function uses, what is its signature (param’s and name) and how will they behave. For example, a header file includes the declaration:
uint8 RS232_Read(uint32 uart_address);
This means that every time we’ll use RS232_Read() we have to put in the UART’s address as a parameter, and the function will return an uint8 value
Whoever is using this function doesn’t really care how it works (implementation).
Listing 6.5. A demonstration of violations of the interface.
Notes: 79
Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 80
#include “io.h”
#include “gui.h”
#include ….
void init ();
void showMenu();
int main()
{
char buffer[120], key;
..
init ();
memset (buffer, 0, sizeof (buffer) );
..
do {
showMenu() ;
key = keypress();
..
}while (stat != EXIT || keypress() != ESC);
return 0;
}
void init ()
{
..
// declerations
#ifndef IO_H
#define IO_H
#define ESC 27
int keypress();
int mousein(..);
..
#endif
// implementations
#include “io.h”
// inputs a key press from the keyboard, 0 for no input
char keyperss()
{
…
}
// imputs mouse’s status ….
int mousein(..)
{
…
main.c
io.h
io.c
Declarations and Definitions (example)
#ifdef / #ifndef / #endif directives:
Done to prevent re-declaration of types, functions variables and constants.
Also useful for adding debugging information and multi-arch support.

## Slide 81: Variables Scope
Every Variable is Defined within some scope.
A Variable’s name and a function’s name are also called symbols
Lexical scopes are defined with curly braces { }. And defines a local area.
The scope written after a Function is the complete body of the function.
Variables defined inside the body of the function are “Local” and only from within that scope they can be accessed.
Variables defined outside the function are Called “Global” and their scope is the hole program .
void p(char x) {
/* p,x */ char y;
/* p,x,y */
char z;
/* p,x,y,z */
}
/* p */
char z;
/* p,z */
void q(char a) { char b;
/* p,z,q,a,b */
{
char c;
/* p,z,q,a,b,c */
}
char d;
/* p,z,q,a,b,d (not c) */
}
/* p,z,q */
(Returns nothing)

## Slide 82
you can declare variables within the body of the function. These variables are called local variables, because they exist only locally within the function itself. When the function returns, the local variables are no longer available (only on the Stack) .
**5.2. local variables and parameters.
Local Variables are visible and usable only within the function in which they are defined.
In C you should define variables only at the beginning of the function. In
C++ you can define variables anywhere within the function, not just at its top.
The scope of the variable is the block in which it is defined.
The parameters passed in to the function are also considered local variables
Local Variables

## Slide 83
**5.2. The use of local variables and parameters.
#include <stdio.h>
#include <inttypes.h>
int add()
{ int a=5;
int b=6;
int sum;
Int mul;
Sum=a+b;
Mul=a*b
return sum + mul;
}
int ret | 0
int argc | 
int **argv | ?
int a | 5
int b | 6
int sum | 0
int mul | 0
The Stack in main(..)
Local Variables
int main(int argc, char **argv)
{
int ret = 0;
add();
return ret;
}
The Stack in add()
int ret | 0
int argc | ?
char **argv | ?

## Slide 84
Variables defined outside of any function have global scope and are available from any function in the program, including main().
**5.3. global and local variables.
#include <stdio.h>
#include <inttypes.h>
int sum=0;
int add_m(int sum1)
{ int a=1;
int b=2;
int mul;
mul=a*b;
sum =sum1+Mul
return sum;
}
int main(int argc, char **argv)
{
add_m(sum);
return 0;
}
int argc | ?
char **argv | ?
Local variables with the same name as global variables do not change the global variables, the Local variable hides the global variable.
Reference to the same variable name within the function will lead to the local variable--not the global one.
Global Variables
int sum | 0
Stack Segment
Data Segment
int sum1 | 0
int a | 1
And so on.. | 
main()
add_m()

## Slide 85
In C\C++, global variables are legal, but they are almost never used.
Global variables are a dangerous but necessary tool. They are necessary because there are times when the programmer needs to make data available to many functions and he does not want to pass that data as a parameter from function to function.
Global’s are dangerous because they are shared data, and one function can change a global variable in a way that is invisible to another function. This can and does create bugs that are very difficult to find.
**5.4 – variables scoped within a block
Global Variable scopes
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 86
In most programming language, functions’ parameters are able to be configured in two ways.
By Value – copies the value to the parameter (which duplicate its value to the parameter of the function). Changes to this parameter will not affect the original variable.
By Reference – works on the original variable itself (which copies the address of the variable to the parameter of the function). Changes will affect the given variable.
In C Programming, passing By-Ref parameters is not supported. It is done in another way. The only way is to send the address’s value (form of by-val):
By-Ref Functions
int main()
{
int a=5;
inc(&a);
}
void inc(int *x)
{
(*x)=(*x) + 1;
}
inc
x
Address of a
main
a
5
main
a
5

## Slide 87
byRef Functions (c++ only)
C++ enables you to send a reference parameter in functions.
The reference copies the address of the symbol when the function is called. Then uses it from within the function (as if the name of the variable is simply changed) .
void myFunction (int &);
int main()
{
int c=10;
printf(“c=%d\n”, c); //output: c=10
myFunction(c);
printf(“c++=%d\n”, c); // output: c++=11
}
void myFunction (int &ref)
{
ref++;
}
// swap in C void swap(int *a1, int *a2); int main() { int x=7, y=11; swap(&x, &y); printf(“x=%d, y=%d, x, y); return 0; } void swap(int *a1, int *a2); { int temp; temp=*a1; *a1=*a2; *a2=temp; } | // swap in C++ void swap(int &a1, int &a2); int main() { int x=7, y=11; swap(x, y); printf(“x=%d, y=%d, x, y); return 0; } void swap(int &a1, int &a2); { int temp; temp=a1; a1=a2; a2=temp; }
//both outputs: x=11, y=7

## Slide 88
Default Parameters (c++ only)
For every parameter you declare in a function prototype and definition, the calling function must pass in a value. The value passed in must be of the declared type. Thus, if you have a function declared as
long myFunction(int);
If the function definition differs, or if you fail to pass in an integer, you will get a compiler error. The one exception to this rule is if the function prototype declares a default value for the parameter.
default value is a value to use if none is supplied. The preceding declaration could be rewritten as
long myFunction (int x = 50);
**5.7 – use of default parameter values
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 89
Overloading Functions (c++ only)
C++ enables you to create more than one function with the same name. This is called function overloading (function polymorphism).
The functions must differ in their parameter list, with a different type of parameter, a different number of parameters, or both.
int myFunction (int, int);
int myFunction (long, long);
int myFunction (long);
The return types can be the same or different on overloaded functions.
**5.8. A demonstration of function polymorphism.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 90
If a variable is valid “within the scope of a function”, what happens when you call that function recursively? Is there more than one “exp”?
#include <stdio.h>
#include <inttypes.h>
float pow(float x, uint32_t exp)
{ /* base case */
if (exp == 0) {
return 1.0;
}
/* “recursive” case */
return x*pow(x, exp – 1);
}
int main(int argc, char **argv)
{
float p;
p = pow(5.0, 2);
printf(“p = %f\n”, p);
return 0;
}
Yes. Each function call allocates a “stack frame” where Variables within that function’s scope will reside.
Recursion
return 5 * pow(5.0, 0);
p = pow(5.0, 2);
return 5 * pow(5.0, 1);
return 1.0
1
5
25
main:
argc, argv ??
P ??
pow:
x 5
exp 2
pow:
x 5
exp 1
pow:
x 5
exp 0
Stack Segment
25
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 91
float pow(float x, uint exp)
{ int i=0;
float result=1.0;
while (i < exp) {
result = result * x;
i++;
}
return result;
}
int main(int argc, char **argv)
{
float p;
p = pow(10.0, 5);
printf(“p = %f\n”, p);
return 0;
}
Solution: “while” loop.
loop:
if (condition) {
statements;
goto loop;
}
while (condition) {
statements;
}
Recursion
**5.10. Demonstrates recursion using the Fibonacci series.
Problem: “recursion” eats stack space (in C).
Each loop must allocate space for arguments and local variables, because each new call creates a new “scope”.
Notes: What about other languages? Some languages such as scheme implement optimized “tail recursion”, which reuses the current stack frame when the recursive call constitutes the last use of the current stack frame. In these cases, recursion costs no more than iteration.

## Slide 92
Arrays

## Slide 93
What Is an Array (1)?
An array is a collection of data storage locations, each of which holds the same type of data. Each storage location is called an element of the array.
For instance
long LongArray[25];
declares an array of 25 elements (type long), named LongArray.
this sets aside enough memory to hold all 25 elements (4 bytes *25=100 bytes) of continuous memory.
Applying sizeof to an array name yields the size of the whole array, in bytes.
Addr | Element
0xf0 | 1st
0xf4 | 2nd
0xf8 | 3th
? | 24th
? | 25th
LongArray[0]
LongArray[1]
LongArray[2]
LongArray[23]
LongArray[24]
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 94
What Is an Array (2)?
Referring to LongArray is a reference to an address in memory (similar to any variable),
However, LongArray is an address, not a value of a type. Which means:
LongArray equals &LongArray which is an address in memory (0xf0…)
You can print that address by printing it:
Printf(“%p”, LongArray);
You can also print an address of a specific element:
Printf(“%p”, &LongArray[2]);
Addr | Element
0xf0 | 1st
0xf4 | 2nd
0xf8 | 3th
? | 24th
? | 25th
LongArray[0]
LongArray[1]
LongArray[2]
LongArray[23]
LongArray[24]
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 95
What Is an Array(3)?
You access each of the array elements by using their index.
the first array element is LongArray[0], LongArray[1] is the second, and so on.
long LongArray[25]; // declaration
For this declaration the existing elements are LongArray[0] - LongArray[24],
LongArray[25] – DOESN’T EXIST!
This is something you need to be aware of,
C will let you access that element !!
**8.1. Using an integer array.
Addr | Element
0xf0 | 1st
0xf4 | 2nd
0xf8 | 3th
? | 24th
? | 25th
LongArray[0]
LongArray[1]
LongArray[2]
LongArray[23]
LongArray[24]
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 96
What Is an Array(4)?
Addr | Element
0xf0 | 1st
0xf4 | 2nd
0xf8 | 3th
? | 24th
? | 25th
LongArray[0]
LongArray[1]
LongArray[2]
LongArray[23]
LongArray[24]
NOTE:
Arrays count from 0, not from 1. This is the cause of many bugs in programs.
Whenever you use an array, remember that an array with 10 elements counts from ArrayName[0] to ArrayName[9]. There is no ArrayName[10].
However the compiler makes a simple offset calculation to get to the desired index, and can easily be set with the incorrect value.
#include <stdio.h>
#define MAX 25
Int main() {
long LongArray[MAX];
LongArray[MAX-1] = 100; // last element
}
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 97
Writing Past the End of an Array
Lets take for instance this declaration:
long LongArray[25];
It has 25 elements, Writing to LongArray[5], which is the sixth element. The compiler multiplies the offset (5) by the size of each element in this case 4.
so it writes to this offset (20) from the beginning of the array.
What if you write to LongArray[50], the compiler ignores the fact that there is no such element. It computes the location (200 bytes) and then writes over whatever is at that location. This might have unpredictable results. If you're lucky, your program will crash immediately, if not it'll take a long time to find the BUG!!
It is so common to write to one past the end of an array that this bug has its own name. It is called a fence post error, (how many fence posts you need for a 10 meter Fence – 9 posts).
**12.2. Writing past
the end of an array.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 98
Initializing Arrays
After the array name, you put an equal sign (=) and a list of comma-separated values enclosed in braces.
int IntegerArray[5] = { 10, 20, 30, 40, 50 };
declares an Integer Array to be an array of five integers. It assigns IntegerArray[0] =10, IntegerArray[1] = 20, and so forth.
int IntegerArray[5] = { 10, 20, 30, 40, 50, 60};
generates a compiler error, 5 elements declared and 6 initialized.
int IntegerArray[5] = { 10, 20};
uninitialized array members will be initialized to 0.
int IntegerArray[] = { 10, 20, 30, 40, 50 };
exactly the same array as you did in the previous example.
Num_of_elements = sizeof(IntegerArray)/sizeof(IntegerArray[0]);
**12.3. Using consts
and enums in arrays.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 99
Multidimensional Arrays
It is possible to have arrays of more than one dimension.
Arrays can have any number of dimensions, although most of the arrays you create will be of one or two dimensions.
A good example of a two-dimensional array is a chess board.
One dimension represents the eight rows; the other dimension represents the eight columns.
char Board[8][8];
**8.5. Creating a
multidimensional array..
Rows columns
x y
x
y
.
.
.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 100
Pointers

## Slide 101
What is a Pointers
A pointer is a variable that holds a memory address.
Every variable has an address. Even without knowing the specific address of a given variable, you can store that address in a pointer.
int Age = 5; int *pAge = NULL; pAge = & Age; => pAge= 0xf002 *pAge = 5
* - pointer
& - address of
pAge is declared to hold the address of an int (variable Age)
When pointers are created, they should be initialized to something. If you don't know what you should assign, assign 0 , this is a NULL pointer.
8.1. Address of variables.
0xF002
pAge
Age
Addr | Value
0xF000 | 0xCC
0xF001 | 0xCC
0xF002 | 0x05
0xF003 | 0x00
0xF004 | 0x00
0xF005 | 0x00
0xF006 | 0xF0
0xF007 | 0x02
0xF008 | ‘c’ 0x62
0xF009 | ‘a’ 0x60
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 102
The Indirection Operator
The indirection operator (*) is also called the dereference operator. When a pointer is used, the value at the address stored by the pointer is retrieved.
A pointer provides indirect access to the value of the variable whose address it stores.
int Age = 5; int *pAge = 0; // 0 = NULL pAge = & Age; Age= 5 *pAge = 5
The indirection operator (*) is also used for declaration, When a pointer is declared, the star indicates that it is a pointer, not a normal variable.
int *pAge=0;
8.2. create a pointer.
Addr | Value
0x000AF000 | 0xCC
0x000AF001 | 0xCC
0x000AF002 | 0x05
0x000AF003 | 0x00
0x000AF004 | 0x00
0x000AF005 | 0x00
0x000AF006 | 0x00
0x000AF007 | 0x0A
0x000AF008 | 0xF0
0x000AF009 | 0x02
0x000AF002
pAge
Age
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 103
Using pointers
Declare a Pointer: write the type of the variable or object whose address will be stored in the pointer, followed by the pointer operator (*) and the name of the pointer.
int * pVar1; int * pVar2 = NULL; // NULL equals to 0 -- #define NULL 0
Assign or initialize a pointer: use the name of the variable whose address is being assigned with the ‘address of’ operator (&).
int iVar = 5, *pVar1 = &iVar, *pVar2; // declaration, the * must be there.. pVar2 = &iVar; // usage, here we set an addr’. no*
/* notice the difference between pVar1 and pVar2 assignment */
Dereference a pointer: use the pointer name with the dereference operator (*) :
int iVar = 5, *pVar1 = &iVar; // declaration (of pVar1) int theValue = *pVar1, *pVar2 = pVar1; // usage (of pVar1)
*pVar2=*pVar1
8.3. Finding out what is stored in pointers.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 104
By-ref parameters
void Func (int byVal, int *byRef);
void main()
{
int a = 5, b = 9;
Func(a, &b);
}
void Func (int byVal, int *byRef)
{
byVal++;
(*byRef)++;
}
a: 0x1200440 | 5
b: 0x1200444 | 9
byVal: 0x1201200 | 5
byRef: 0x1201204 | 0x1200444
main()
Func()
a: 0x1200440 | 5
b: 0x1200444 | 10
main()
After Func execution
Before Func execution
In Func execution

## Slide 105
char * get_pointer()
{ char x=0;
return &x;
}
int main()
{
char *ptr = get_pointer();
*ptr = 12; /* valid? */
other_function();
}
ptr points to a location that’s no longer in use, and will be reused the next time a function is called!
Invalid pointers
A pointer to a variable allocated on the stack becomes invalid when that variable
goes out of scope and the stack frame is “popped”.
The pointer will point to an area of the memory that may later get reused and rewritten
A Valid pointer is one that points to memory that your program controls.
Using invalid pointers will cause non-deterministic behavior, and will often cause the Operating system (Linux) to kill your process (SEGV or Segmentation Fault) if you are lucky.

## Slide 106
Strings

## Slide 107: Strings (1)
Strings in C are defined as arrays of characters.
For example, the following defines a string of 50 characters:
char name[50];
C has no string handling facilities built in. This means that intuitive operations such as:
char firstname[50],lastname[50],fullname[100];
firstname= "Arnold"; /* Illegal */
lastname= "Schwarznegger"; /* Illegal */
fullname= "Mr"+firstname +lastname; /* Illegal */
However, there’s a special library of strings handling routines <string.h> (or the newer <cstring>), with which such operations are done.

## Slide 108: Strings (2)
Assigning the \0 character to some item in the array turns it from an ordinary array of chars to a C string, so that it’s ready for use of string.h routines.
\0 is used to indicate the end of string (not the memory allocation). If we store the word “DAVE” in it, its contents will look like:
This means that in terms of strings, the length of that string is 4, not including the null, although the memory it occupies is of 50 chars.
Length size is achieved by using the strlen() function
D
A
V
\0
E

## Slide 109: Strings Initializations
char name [7] = “DavidG“;
Typically, a compiler sets aside an area in memory (string and text literals area) to hold all the quoted strings used in the program source code, associating each stored string with its address. In our case, this enables name to serve as another synonym to the address where "DavidG" lies, (just as DavidG is a pointer to that address).
char name [] = “DavidG“;
char name [] = {‘D’, ‘a’, ‘v’, ‘i’, ‘d’, 'G', ’\0’};
char* name = “DavidG”; //?? Is it really allowed

## Slide 110: Strings Initializations
#include <stdio.h>
#include <string.h>
void strExample();
int main()
{
printf(“str %s”, “Example”);
strExample();
printf(“goodbye”);
return 0;
}
void strExample()
{
char *str1 = “str-1”;
char str2[12] = “str-2”;
}
0x00
0x40
0x44
0x20
‘s’
‘t’
‘r’
‘-’
‘2’
‘\0’
‘s’
‘t’
‘r’
‘ ‘
‘%’
‘s’
‘\0’
‘E’
‘x’
‘a’
‘m’
‘p’
‘l’
‘e’
‘\0’
‘s’
‘t’
‘r’
‘-’
‘1’
‘\0’
‘s’
‘t’
‘r’
‘-’
‘2'
‘\0’
breakpoint
0x00ff00d0: (char *) str1 = 0x00404420
sizeof(str1) = 4 bytes
0x00ff00cc: (char [12]) str2 = “str-2”
sizeof(str2) = 12 bytes
0x00404420: (char *) = “str-1”
0x0040441a: (char *) = “str-2”
duplicated to strExample()
0x00404414: (char *) = “goodby”
0x00404428: (char *) = “Example”
0x0040442f: (char *) = “str %s”
Stack
Segment
Data
Segment

## Slide 111: Const for Pointers
What’s the difference?
Pointers to arrays : char x[ ] vs. char* x
<type>[ ] belongs to the category of char* const ptr.
char name* = " abc..." belongs to the category of const char* ptr .
char* const ptr - ptr is a pointer to a constant address. ptr isn't allowed to point to any other address.
const char* ptr - ptr currently points to a constant content, which is not allowed to be modified. However, ptr is allowed to point to somewhere, .
const char* const ptr - ptr is a pointer to a constant address, and the content in that address is constant.

## Slide 112: Pointers to arrays
What’s the difference?
Pointers to arrays : char x[ ] vs. char* x
x is of type char[]. Therefore, ptr can't be changed and operators attempting to do so, such as: x++ or x-- are illegal.
char* x is much the same, only that sizeof(name) the number of elements, is decided by the programmer rather than letting the compiler do that automatically as is on the first case.
The third initialization causes name to be a pointer of type const char* ptr meaning that name can be assigned to point at other addresses, but this current address is unchangeable. The memory space is allotted and written once, when initialized, and further changes to it are illegal:
const char* name = “DavidG”; //recommended usage of const
name[2] = 'd'; //illegal. No change permitted
name++; //legal, but cautious
strcpy(name,"gameover"); //buffer overflow,
strcpy //must use strings with finite length

## Slide 113: (char), (char *), (char[])
If you are having a little problems putting it all together … let’s practice:
char ch = ‘a’, ch_array[5] = “abcd”, *ch_ptr = ch_array;
The variable ch is type: _______ and to print it write: printf(“__”, ch);
The variable ch_array is type: _______.
  Printing a char in the array: printf(“___”, ___); and the printed type is: ______
  Printing the array (string assumed): printf(“___”, ___); and the printed type is: _____
  According to the way the array was defined it is positive that ch_array[4]=__
  What will be printed by that? printf(“%s %s %s”, ch_array, ch_array+2, &ch_array[2]);
  Will the result of printing ch_array ‘s address is the same as printing &ch_array ? ___. Do it!
  What will be the result of trying to compile the next line: ch_array++; __________________________________________________________
The variable ch_ptr is type: _______ . To print that pointer: printf(“__”, ____);
  Printing a character using ch_ptr: printf(“___”, ___); and the printed expression’s type _____
  Will the result of printing ch_ptr ‘s address is the same as printing &ch_ptr ? ___. Do it !
  Printing ch_ptr as defined earlier is ____’s address. printing &ch_ptr is ____’s address.
  What will be the result of trying to compile the next line: ch_ptr++;
  What will be the resault of printf(“%s”, ch_ptr); after ch_ptr++;

## Slide 114: Useful string.h routines
Gets the string length
size_t strlen ( const char* str );
Returns the length of str: the amount of characters between the beginning of the string and the terminating null character.
Copy strings
char* strcpy( char* destination, const char* source );
Copies the C string pointed by source into the array pointed by destination, including the terminating null character.
Notes:
To avoid overflows, the size of the array pointed by destination shall be long enough to contain the same C string as source (including the terminating null character), and should not overlap in memory with source.
Related functions:
char* strncpy ( char* dest, const char* source, size_t num);
similar to strcpy but copies only the first num characters of source to dest.
**strlen_examp.cpp

## Slide 115: Useful string.h routines
Concatenate strings
char* strcat ( char* dest, const char* source );
Appends a copy of the source string to the dest string. The terminating null character in dest is overwritten by the first character of source, and a new null-character is appended at the end of the new string formed by the concatenation of both in destination.
Compare two strings
int strcmp ( const char* str1, const char* str2 );
Compares the C string str1 to the C string str2.
starts comparing the first character of each string. If they are equal to each other, it continues with the following pairs until the characters differ or until a terminating null-character is reached.
Return values: positive : str1>str2
      zero: str1 = = str2 (contents, not addresses!)
      Negative: str1<str2
Related functions:
int strncmp ( const char* str1, const char* str2, size_t num );
Similar to strcmp but compares up to num characters defined
**strcat_examp.cpp

## Slide 116: Working Strings on bytes resolution
There's the option to manipulate all the above routines, copying, concatenating and comparing straightforward on the raw bytes those strings are pointing to Fill block of memory
void* memset ( void* ptr, int value, size_t num );
Sets the first num bytes of the block of memory pointed by ptr to the specified value (interpreted as an unsigned char).
Example
#include <stdio.h>
#include <string.h>
int main ()
{
  char str[] = "almost every programmer should know memset!";
  memset (str,'-',6);
  puts (str); // well, don’t panic .. puts(..) is the same as printf(“%s” ..)
  return 0;
}
//output: ------ every programmer should know memset!

## Slide 117: Strings on bytes resolution-cont’d
Copy block of memory
void* memcpy ( void* dest,const void* source, size_t num );
Notes:
Copies the values of num bytes from the location pointed by source directly to the memory block pointed by destination.
binary copy of the data: type of the objects are irrelevant
Always copies exactly num bytes. Beware of data overflows!
for overlapping memory blocks, memmove() is a safer approach. It does the same but copying takes place as if an intermediate buffer was used, allowing the dest and source to overlap.
**memcpy_examp.cpp

## Slide 118: Strings on bytes resolution-cont’d
Compare two blocks of memory
int memcmp ( const void* ptr1, const void* ptr2, size_t num );
Similar to strcmp, doing so directly byte by byte. See references for further details.
And Many More…
atoi - Convert string to integer
#include <ctype.h>
tolower/upper – turns a given character to lower/uppercase letters
isalpha - Check if character is alphabetic
isdigit - Check if a character is a decimal digit
You're invited to try implementing some of them by yourself …

## Slide 119
Dynamic Memory
Allocation
119

## Slide 120
The Free Store (Heap)
The Memory is divided into 5 main areas (for now )
- Registers - Used for internal housekeeping functions, such as keeping track of the top of the stack and the instruction pointer - Stack Seg (SS) - Local variables, along with function parameters. - Data Seg (DS) - Global variables, But contains more segments. - Code Seg (CS) - Where the Code is run from - The free store (aka Heap) - Just about all remaining memory is given to the heap
A problem we might run into without the Heap…
Local variables are valid as long as you are in the defining function, when the function returns, the local variables are thrown away.
Global variables solve that problem at the cost of unrestricted access throughout the program, which leads to a difficult code to understand and maintain.
Putting data in the free store solves both of these problems.
Heap
GVars
BSS
SS
DS
CS
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 121
Why Do we need the Heap?
Suppose you want to create a String Array representing someone's last name. The simplest way is to use a character array member to hold the name.
But this has some drawbacks. You might use a 14-character array and then run into ‘Bartholomew Smeadsbury-Crafthovingham’. Or, to be safer, you may use a 40-character array.
But, if you then create an array of 2000 such Strings, you'll waste a lot of memory with character arrays that are only partly filled. (At this point, we're adding to the computer's memory load.)
There is an alternative. Often it is much better to decide many matters, such as how much storage to use, in Real Time when a program is running
The usual approach is to make a dynamic allocation for the correct amount of memory while the program is running.
The allocation\de-allocation could be quite tricky at times (why?)
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 122
The Free Store (Heap)
The stack is cleaned automatically when a function returns. All the local variables go out of scope, and they are removed from the stack.
The free store is not cleaned until your program ends, and it is your responsibility to free any memory that you've reserved when you are done with it.
The memory you reserve remains available until you explicitly free it.
If you reserve memory on the free store while in a function, the memory is still available when the function returns.
Accessing memory in this way, rather than using global variables, is that only functions with access to the pointer have access to the data. This provides a tightly controlled interface to that data, and it eliminates the problem of one function changing that data in unexpected and unanticipated ways.
For this to work, you must be able to create a pointer to an area on the free store and to pass that pointer among functions.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 123
malloc
Allocates memory block on the free store, returning a pointer to the beginning of the block.
If malloc() cannot create memory on the free store (memory is, after all, a limited resource) it returns the null pointer.
#include<stdlib.h>
void * malloc ( size_t size );
size - Size of the memory block, in bytes.
The content of the newly allocated block of memory is not initialized, remaining with indeterminate values.
To create an unsigned short variable on the heap:
Char *ptr = (char *) malloc(sizeof(char));
ptr - return value from malloc is the memory address and It must be cased to the pointers type.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 124
malloc (continued)
To create an int variable on the free store, you might write
int *pPointer;
pPointer = (int*) malloc(sizeof(int));
if(NULL==pPointer)
{
Printf(“error allocating Memory”);
return (-1);
}
*pPointer = 72;
This means, "Put 72 to the address on the free store to which pPointer points.“
Always check your pointer for NULL.
If malloc() cannot create memory on the free store let the programmer know and act accordingly..
Notes: 124
Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 125
realloc
To create a dynamic array, simply allocate N elements * sizeof(type) that you need.
int *pPointer, N=5;
pPointer = (int*) malloc(sizeof(int));
if(NULL==pPointer)
{
Printf(“error allocating Memory”);
return (-1);
}
pPointer = (int *) realloc(pPointer, N*sizeof(int));
…
Using a pointer is basically working with an address, same as working with arrays.
Dynamically allocated arrays are treated the same way as regular arrays.

## Slide 126: Free (void *ptr)
When you are finished with your area of memory, you must call free on the pointer.
free de-allocates (returns) the memory to the free store.
#include <stdlib.h>
void free(void *ptr);
Notes:
the pointer itself is a local variable. When the function in which it is declared returns, that pointer goes out of scope and is lost.
The memory allocated with malloc is not freed automatically, if That memory becomes unavailable a situation called a memory leak occurs. It's called a memory leak because that memory can't be recovered until the program ends.
To restore the memory to the free store, you use the keyword free system call.
free (pPointer);
pPointer=NULL; //always zero it
** 8.5 allocating variables on the heap

## Slide 127
Pointer calculations
What happens if we add 1 to a pointer that points to a variable of some type ?
int *pHeap = NULL;
pHeap = (int *)malloc(sizeof(Array));
*(pHeap+1) // increased by 1 byte?? NO it by 4=sizeof(int)
The pointer is incremented by the size of the variable type it points to.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 128: malloc \ free – Warnings
Each time you allocate memory you must check to make sure the pointer is not null) there was enough memory in the pool to allocate).
Stray /Dangling pointers :
  When you delete a pointer, the memory it points to is freed. Calling delete on that pointer again will crash your program! When you delete a pointer, set it to zero (null).
  Using a pointer after freeing it without nullizing it, will the program to be unstable (or crash the program). Calling delete on a null pointer is guaranteed to be safe.
Memory leaks :
  For every time in your program that you allocate memory, there should be a call to de-allocate it.
  Use caution when allocating memory inside a function and exiting that function freeing the allocated memory
  char *pChar = malloc(sizeof(char));
  free (pChar) ; //frees the memory
  pChar = 0; //sets pointer to null

## Slide 129
Memory Leaks
Another way you might inadvertently create a memory leak is by reassigning your pointer before deleting the memory to which it points.
Consider this code fragment:
int *ptr = (int *) malloc(sizeof(int));
*ptr = 72;
ptr = (int *) malloc(sizeof(int)); //new address!!
* ptr = 84; //WRONG
The code should have been written like this:
int *ptr = (int *) malloc(sizeof(int));
*ptr = 72;
free ptr;
ptr = (int *) malloc(sizeof(int)); // allocate new Memory space from O.S.
*ptr = 84;
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 130
130
Arrays on the Free Store
Nothing new here use malloc, sizeof and casting as usual
pHeap = (int *)malloc(sizeof(Array)); //pHeap points to 1st Element
declares pHeap to be a pointer to an array on the heap.
In order to access Array’s elements on the heap we increment the pointer (the Compiler know how to calculate the offset)
*pHeap = 10; // set 1st Element to 10
pHeap ++; // advance to 2nd Element
*(pHeap +2) = 20; // set 4th Element to 20
** 8.6 allocating an array on the heap
Notes: 130
Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 131
131
Deleting Arrays on the Free Store
In order to delete the array on the heap we use free as usual:
  free (pHeap );
  pHeap = NULL;
this returns all the memory set aside for the array back to O.S., and forbids from Stray /Dangling pointers
Notes: 131
Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 132
Stray or Dangling Pointers
One source of bugs that are nasty and difficult to find is stray pointers.
A stray pointer is created when you call free on a pointer-thereby freeing the memory that it points to, and later try to use that pointer again without reassigning it.
be careful not to use a pointer after you have called delete on it. The pointer still points to the old area of memory, but the compiler is free to put other data there; using the pointer can cause your program to crash. Worse, your program might proceed merrily on its way and crash several minutes later.
To be safe, after you delete a pointer, set it to null (0).
**8.4. Creating a stray pointer.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 133
Dynamic Memory-Sum it up (Heap)
Dynamic memory is useful.
Part of C strategy is letting the program decide about memory during runtime rather than during compile time. That way, memory use can depend on the needs of a program instead of upon a rigid set of storage-class rules. Dynamic memory has several caveats:
Whereas the stack is automatically reclaimed, dynamic allocations must be tracked and free()’d when they are no longer needed. With every allocation, be sure to plan how that memory will get freed. Losing track of memory is called a “memory leak”.
Reference counting
Whereas the compiler enforces that reclaimed stack space can no longer be reached, it is easy to accidentally keep a pointer to dynamic memory that has been freed. Whenever you free memory you must be certain that you will not try to use it again. It is safest to erase any pointers to it.
Because dynamic memory always uses pointers, there is generally no way for the compiler to statically verify usage of dynamic memory. This means that errors that are detectable with static allocation are not with dynamic
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 134
Copyright @ 2007 Real Time College
134
Arguments to main

## Slide 135: argc & argv what are they ?
Copyright @ 2007 Real Time College
135
The declaration of main looks like this:
int main(int argc, char *argv[]);
There are two arguments to main: argc and argv.
argc - is a count of the arguments supplied to the program.
argv - is an array of pointers to strings.
These arguments are passed to the program by the host system's command line
interpreter
you will often see the declaration of main expressed in these terms as well:
int main(int argc, char **argv);

## Slide 136
Copyright @ 2007 Real Time College
136
When a program starts, the arguments to main will have been initialized to meet the following conditions:
argc is greater than zero.
argv[argc] is a null pointer.
argv[0] through to argv[argc-1] are pointers to strings whose meaning will be determined by the program.
argv[0] will be a string containing the program's name or a null string if that is not available.
Remaining elements of argv represent the arguments supplied to the program. In
cases where there is only support for single-case characters, the contents of these
strings will be supplied to the program in lower-case.
argc & argv what are they ?

## Slide 137
Pointers to Functions

## Slide 138: Pointers to Functions (1)
A function's name is actually a const pointer to that function.
When alternative functions may be used to perform similar tasks on data. You can pass the data and the function to be used to some control function for instance.
Declaration:
1. long (* pFunc)(int);
2. long* Func (int);
Question: What’s the difference?
The second declaration –Func is a function which gets an int and returns a pointer to type long variable.
The first declaration- pFunc is a pointer to function which gets an int and returns a type long result.

## Slide 139: Pointers to Functions (2)
long (*)(int)is a type just like any other types: int*, char, enum color* .
  pFunc is a pointer of such type.
  If it's too long for you, replace it by typedef in this manner:
typedef long(*LPF)(int, int); // the type is shortly called LPF
Invoking the function by the pointer, Both are equivalent.
pFunc(x);
(*pfunc)(x);
We can use the pointer to invoke a specific function once it's assigned to point at some actual function:
long (* pFunc1) (int, int);
long someFunc (int, int);//implemented somewhere
pFunc1 = someFunc; //pointers assignment
pFunc1(5,7);
** 11.1 pointer to functions
** 11.2 pointer to functions

## Slide 140
Structures

## Slide 141: Structures
Structure is a method of packing data of different types, a convenient method of
handling a group of related data items of different data types.
A structure type is defined by
struct struct-name
{
type field-name;
type field-name; ...
}
Example:
struct lib_books
{
char title[20];
char author[15];
int pages;
float price;
};
Another example:
struct student_type
{
char name[20];
int ID;
}

## Slide 142: Structures
Copyright @ 2007 Real Time College
142
the keyword struct declares a structure to holds the details of four fields namely title, author pages and price.
Each member may belong to different or same data type.
The structure we just declared is not a variable by itself but a template for the
structure (a type)
We can declare variables of this structure by
struct lib_books book1,book2,book3;
declares book1,book2,book3 as variables of type struct lib_books each declaration has four elements of the structure lib_books..
You can make the the structure into a type:
typedef struct lib_books { …. } lib_books_t

## Slide 143: Accessing Structure members Directly
Copyright @ 2007 Real Time College
143
to declare a variable of the Structure and access a member, use the operator ‘.’ Which is known as dot operator or period operator.
lib_books book1;
book1. price = 15;
strcpy(book1.title,”basic”);
strcpy(book1.author,”Balagurusamy”);
book1.pages=250;
**Lesson-12.1

## Slide 144: Accessing Structure members Indirectly
Copyright @ 2007 Real Time College
144
To declare a pointer variable of the Structure and access a member within the class, use the operator ‘->’.
lib_books book1,*ptr_book1 = &book1;
ptr_book1-> price = 15;
strcpy(ptr_book1-> title,”basic”);
strcpy(ptr_book1-> author,”Balagurusamy”);
ptr_book1-> pages=250;
**Lesson-12.2
**Create an Employee managing program

## Slide 145
Copyright @ 2007 Real Time College
145
To declare a pointer variable of the Structure and access a member within the class, use the operator ‘->’.
lib_books book1, book2 = {30, “IT”, “Stiven King”, 300};
book1.price = 15;
strcpy(book1.title,”basic”);
strcpy(book1.author,”Balagurusamy”);
book1.pages=250;
Init Structures
**Lesson-12.2
**Create an Employee managing program

## Slide 146
Accessing Data Members
For an instance of an object - You accessed data members and functions by using the
dot (.) operator
For a ptr to an instance of an object (access the object on the free store),
C/C++ provides a shorthand operator for indirect access:
the points-to operator (->),
pCat->GetAge();
You can also use
(*pCat).GetAge();
Parentheses are used to assure that pCat is dereferenced before GetAge() is accessed.
**8.6 accessing member variables on the free store.
Notes: Variables declared ‘static’ inside of a function are allocated only once, rather than being allocated in the stack frame when the function is called. Static variables therefore retain their value from one call to the next, but may cause problems for recursive calls, or if two threads call the function concurrently.
Java users:
Just to be aware: recursion doesn’t always work in Java because objects are always passed by reference (i.e they are not copied). In java, this recursive function would only work if it was a primitive type like int being passed.

## Slide 147
/* allocating a struct with malloc() */
struct my_struct *s = NULL;
s = (struct my_struct *)malloc(sizeof (my_struct))); if (s == NULL) {
printf(stderr, “no memory!”);
exit(1);
}
memset(s, 0, sizeof(my_struct));
/* another way to initialize an alloc’d structure: */
struct my_struct init = {
counter: 1,
average: 2.5,
in_use: 1
};
/* when you are done with it, free it! */
free(s);
s = NULL;
malloc() does not zero the memory, so you should memset() it to 0.
Always check for NULL.. Even if you just exit(1).
malloc() allocates n bytes
Why?
Use pointers as implied in-use flags!
Dynamic Memory Allocation of Structures
Notes: What to do when malloc fails?
Except in certain cases, it’s going to be very difficult to recover from this state because lots of functions will start failing and the correct way to handle these errors is not obvious. If you continue without your memory, it is likely that your program will get into some very seriously broken state.
The main case where recovery IS possible is the case that the malloc() that failed is part of a single too-large transaction that can fail independently of the rest of the system. For example if the user asks your program to allocate a zillion bytes and you can’t, just abort that request and ask for the next request. But if your system is just generally out of memory, there’s not much you can do.
In emstar, processes automatically respawn and the system is generally designed to handle module failures, so a slow memory leak that causes you to exit and restart may allow a fairly graceful recovery.
Memmove
memmove() is written so that it will copy in the correct order to be able to shift data in a buffer, that is, if the source and destination buffers overlap. This is not true of the memcpy() function.
Use pointers as implied in-use flags!
One clever way to reduce the number of state variables is to avoid the use of “in use” flags when there is also a pointer that can be NULL. That is, if the item is not allocated (and therefore a NULL pointer), it’s not in use. If there’s a pointer there, then you assume that it is valid, initialized, etc. By avoiding this redundancy of state varaibles, you avoid the various cases where the two variables are out of sync.. Pointer there but not in use.. Or in use but no pointer.

## Slide 148: Pragma directive
Copyright @ 2007 Real Time College
148
The Compiler generates 32-bit code, and in that mode, there is a significant
penalty (in terms of run-time performance) for unaligned accesses, like accessing
a 16-bit short which isn't aligned on a 16-bit word boundary, or accessing a 32-bit
int which isn't aligned on a 32-bit dword boundary.
To produce faster code, The Compiler pads struct members so that each one can
be accessed without delays; this sometimes produces struct size which is larger
than the sum of the sizes of its members. If you need to configure the exact struct
with no padding you can use one of these directives used for that purpose:
Visual Studio: #pragma pack(1);
GCC Linux: use the __attribute__((packed)) extension
This will prevent The Compiler from padding the structure members; this will
make accesses to some of the members significantly slower.
**Lesson-12.3

## Slide 149
Bitwise Operations

## Slide 150: Bitwise Operations
Usage:
  data compression & encoding
  Optimize computations
  Many programs (e.g. systems type applications) must actually operate at a low level where individual bits/bytes must be operated on.
  The combination of pointers and bit-level operators makes C useful for many low level applications and can almost replace assembly code. (Only about 10 % of UNIX is assembly code the rest is C!!!)

## Slide 151: Bitwise Operations
OR |  | 
X¦Y | Y | X
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
1 | 1 | 1
XOR |  | 
X^Y | Y | X
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
Table: Bitwise operators | 
Bitwise AND | &
Bitwise OR | ¦
Bitwise XOR | ^
Bitwise NOT | ~
Shift left | <<
Shift right | >>
AND |  | 
X&Y | Y | X
0 | 0 | 0
0 | 1 | 0
0 | 0 | 1
1 | 1 | 1

## Slide 152: Bitwise Shift Operators
The shift operators shift their first operand left (<<) or right (>>) by the number of positions the second operand specifies.
x=0x1
  y= x<<1 => y= 0x2
  y= x>>1 => y=0x0
You can also mean to
Multiply by 2 => shift left
Divide by 2. => shift right
Example 1:
//shift left
int main()
{
  int i =1;
  int j =i<<5;
  printf("%d\n",j);
}
**Lesson-13.1
**Lesson-13.2

## Slide 153: Changing Specific Bits
Copyright @ 2007 Real Time College
153
//set Register’s bit 5 to Down state
//set Register’s bit 3 to Up state
Example 2:
#define BitDown 5
#define BitUp 3
int main()
{
//in order to access Register we must declare a pointer to it
int* preg = (int*)REG_ADDR;
//set to zero the bit 5
*preg &= ~(1<<BitDown);
//set to one bit 3
*preg |= (1<<BitUp);
return 0;
}
**Lesson-13.1
**Lesson-13.2

## Slide 154: Read Modify Write
Accessing and setting specific bits is often termed as a read modify write access, since you don’t want to change the whole byte but just specific bits
For instance:
(see the last page) setting bit 5 down and bit 3 up in some register, stored at address REG_ADDR.
Suppose we want to assign bits[12:6] from some 16bit source register, to bits [6:0] of another 16bit target register.
[3:0] | [7:4] | [11:8] | [15:12] | 
1010 | 1011 | 1100 | 1101 | Source
1101 | 1100 | 1011 | 1010 | Target
0010 | 1111 | 1011 | 1010 | Result

## Slide 155
Big & Little Endians

## Slide 156: Big Endian
Embedded Architectures differ in the way they store data in memory.
Two methods are used Big Endian and Little Endian
Examples of storing the value 0x0A0B0C0D in memory:
In Big-Endian the most significant byte (MSB) value, which is 0x0A in our example, is stored at the memory location with the lowest address, the next byte value in significance, 0x0B, is stored at the following memory location and so on. This is akin to Left-to-Right reading in hexadecimal order.
Architectures such as Motorola, MIPS use this method
Addr | Value
0xF000 | 0x0A
0xF001 | 0x0B
0xF002 | 0x0C
0xF003 | 0x0D
0xF004 | 

## Slide 157: Little Endian
storing the same value 0x0A0B0C0D in memory:
Littel-endian
The least significant byte (LSB) value, 0x0D, is at the lowest address. The other bytes follow in increasing order of significance.
Architectures such as Intel use this method
Addr | Value
0xF000 | 0x0D
0xF001 | 0x0C
0xF002 | 0x0B
0xF003 | 0x0A
0xF004 | 
Question: write a function that returns true if the Architecture is Big-Endian else false if its Little Endian.

## Slide 158: Endianness in networking
Networks use Big-Endian order, and thus it is called network order.
when sending information over a network in a common format. the Internet Protocol defines a standard big-endian network byte order. This byte order is used for all numeric values in the packet headers and by many higher level protocols and file formats that are designed for use over IP.
The Berkeley sockets API defines a set of functions to convert 16- and 32-bit integers to and from network byte order: the htonl (host-to-network-long) and htons (host-to-network-short) functions convert 32-bit and 16-bit values respectively from machine (host) to network order; whereas the ntohl and ntohs functions convert from network to host order.
Embedded
System
Embedded
System
Network
htons(..)
htonl(..)
ntohs(..)
ntohl(..)

## Slide 159
Bit Fields & Unions

## Slide 160: Bit-Fields
We use bit fields as an effective alternative approach for storing and modifying data on a bit resolution instead of using masks & bitwise operators.
typedef struct Bit {
char f1:1 ;
}Bit;
typedef struct Byte
{
Uchar f1:1 ;//LSB
Uchar f2:1 ;
Uchar f3:1 ;
Uchar f4:1 ;
Uchar f5:1 ;
Uchar f6:1 ;
Uchar f7:1 ;
Uchar f8:1 ;//MSB //sizeof()= 1 byte
}Byte;
**bitFields_examp.cpp

## Slide 161: BitFields –cont’d
Access members as in usual structures:
  Byte MyByte.f2 =1;
  Byte* pMybyte = &MyByte;
  pMybyte->f2 = 0;
type of bit field must be large enough for number of bits in that field.
The first declared fields are the LSBs (in case it's little endian).
Bit fields are always converted to integer type for computation.
The unsigned definition is important - ensures that no bits are used as a
+ - flag.

## Slide 162: BitFields –cont’d
A more “embedded" motivation:
Frequently device controllers (e.g. disk drives) and the operating system need to communicate at a low level. Device controllers contain several registers which may be packed together in one integer.
command | sector | track | Error code |  |  |  | error | ready
5bits | 5bits | 9bits | 8bits | 1bit | 1bit | 1bit | 1bit | 1bit
Write protection
Disk spinning
Head loaded

## Slide 163: BitFields –cont’d
typedef struct DISK_REGISTER
{
unsigned ready:1;
unsigned error_occured:1;
unsigned disk_spinning:1;
unsigned write_protect:1;
unsigned head_loaded:1;
unsigned error_code:8;
unsigned track:9;
unsigned sector:5;
unsigned command:5;
} DISK_REGISTER ;

## Slide 164: BitFields –cont’d
To access values stored at a particular memory address, DISK_REGISTER_MEMORY we can assign a pointer of the above structure to access the memory via:
DISK_REGISTER* disk_reg = (DISK_REGISTER *)DISK_REGISTER_MEMORY;
The disk driver code to access this is now relatively straightforward:
  /* Define sector and track to start read */
  disk_reg->sector = new_sector;
  disk_reg->track = new_track;
  disk_reg->command = READ;
  /* wait until operation done, ready will be true */
  while ( ! disk_reg->ready ) ;
  /* check for errors */
  if (disk_reg->error)
  { /* interrogate disk_reg->error_code for error type */
  switch (disk_reg->error_code)
  ...... }

## Slide 165: BitFields – Notes of Caution
Sizeof(): there's no way to get the size of a certain bit field, sizeof(MyByte.f2) neither at run-time nor at compile time.
Portability:
  sizeof(struct x) : in general, sizeof(struct) may be larger than the expected memory sum of its members because compilers tend to pad spaces in order to align all members to the optimal alignment CPUs best work with. (Optimal – in terms of speed and storage management efforts invested on the data type, whenever it's accessed to read/write).
  In order to force the compiler to pack data the way we want, there's a set of complier's directives: #pragma pack(n), __unaligned and more… note however that misaligned variables not in their natural boundaries may result in slower performances, and an effort of the OS to handle fix ups.

## Slide 166: BitFields -Notes of Caution-cont’d
sizeof(struct BitStrct): the amount of space such bit fields occupy and the policy used to align them in memory is very compiler ( and sometimes OS) dependent. Some compliers pack all fields as compact as they can (when not all of the space of type of bit field was used), some do not.
Big/little endian: Some bit field members are stored left to right others are stored right to left in memory.
If portability of code is a premium, you can use bit shifting and masking to achieve the same results but not as easy to express or read.
more details about alignment policies:
http://publib.boulder.ibm.com/infocenter/lnxpcomp/v8v101/index.jsp?topic=/com.ibm.xlcpp8l.doc/proguide/ref/calgnbit.htm

## Slide 167: Unions
A union, is a collection of variables of different types, just like a structure. However, with unions, you can only store information in one field at any one time.
The size of a union is equal to the size of it's largest data member
Assigning a value to its biggest member will consequently overwrite all the values of the rest of the members.
Example 1:
//declaration+ instantiation of some union "at one shot"
  union time{
  long simpleDate; //[sec] double perciseDate; //[msec]
  }mytime;
Accessing is the same as in structures:
. . . printTime( mytime.perciseDate ); . . .
**union_examp1.cpp

## Slide 168: Unions-cont’d
A more “low level” motivation:
c[0] [7:0] | c[1] [15:7] | c[2] [23:16] | c[3] [31:24]
lo[15:0] |  | hi[31:16] | 
Long[31:0] |  |  | 
mix
union mix_t {
long l;
struct {
short lo;
short hi;
} s;
char c[4];
} mix;
**union_examp2.cpp

## Slide 169: Unions-Notes of caution:
In the above example, we must be sure that our compiler allocates the same size to the long and the struct’s members, so that they really share the entire same memory space.
Big/little endian - We also need to confirm the order of MSBs/LSBs of the fields inside the union.
The exact alignment and order of the members of a union in memory is platform dependant. Therefore be aware of possible portability issues with this type of use.

## Slide 170
IO commands

## Slide 171: Basic IO commands (1)
Background
Input device: Any object which produces a stream of bits, that can be read in into the program serially: keyboard, files (on Disk) , NIC, etc..
Output device: any object which knows how to receive bits stream, into which this bits can be fed serially :screen, files (on Disk), NIC
A C application can "speak" with several IO devices.
streams
Streams are a portable way of reading and writing data. They provide a flexible and efficient means of I/O.
A Stream is a file or a physical device (e.g. printer or monitor) which is manipulated with a pointer to the stream.

## Slide 172: FILE structure
FILE is the main file control structure for streams. The exact structure of it is very platform-dependent, so ANSI C proposes that the exact structure of this structured type should not be known, and well-written programs do not need to access the internal fields of this structure.
typedef struct {
char *fpos; /* Current position of file pointer (absolute address) */ void *base; /* Pointer to the base of the file */ unsigned short handle; /* File handle */ short flags; /* Flags (see FileFlags) */ short unget; /* 1-byte buffer for ungetc (b15=1 if non-empty) */ unsigned long alloc; /* Number of currently allocated bytes for the file */ unsigned short buffincrement; /* Number of bytes allocated at once */ } FILE;
enum FileFlags {_F_READ = 0x0001, _F_WRIT = 0x0002, _F_RDWR = 0x0003, _F_ERR = 0x0010, _F_EOF = 0x0020, _F_BIN = 0x0040};

## Slide 173: FILE API’s
Opening and Closing Files:
FILE *fopen(const char *path, const char *mode);
int fclose(FILE * stream);
Basic Reading and Writing:
size_t fread( void *ptr, size_t size, size_t nmemb, FILE *stream);
size_t fwrite( const void *ptr, size_t size, size_t nmemb,FILE *stream);
Status Functions:
void clearerr( FILE *stream);
int feof( FILE *stream);
int ferror( FILE *stream);

## Slide 174: Basic IO commands (2)
There exists an internal C data structure, FILE, defined in stdio.h which identifies a stream and contains the information needed to control it, including
  a pointer to its buffer.
  its position indicator
  its state indicators.
We simply need to refer to the FILE structure in C programs when performing I/O with streams.
We just need to declare a variable or pointer of this type in our programs.
We do not need to know (at this stage) any more specifics about this definition. The program doesn't even know at runtime where its standard devices are linked to, it's the OS responsibility.
We must open a stream before doing any I/O, then access it and then close it.
Stream I/O is BUFFERED: That is to say a fixed "chunk'' is read from or written to a file via some temporary storage area (the buffer).

## Slide 175: Basic IO commands (3)
Note:
data written to a buffer does not appear in a file (or device) until the buffer is flushed or written out. (\n does this or endl in C). Any abnormal exit of code can cause problems.
A data can be flushed “manually” using fflush(FILE*) command.

## Slide 176: Standard streams
UNIX defines 3 predefined streams (in stdio.h):
stdin, stdout, stderr -They all use text as the method of I/O.
stdin and stdout can be used with files, programs, I/O devices such as keyboard, console, etc..
stderr always goes to the console or screen.
The console is the default for stdout and stderr.
The keyboard is the default for stdin.
Predefined streams are automatically open. When we run the program, we can temporarily change the IO devices with which it communicates by redirection:
hello < infile.txt > outfile.txt
prog1 | prog2
out | lpr
The basic lib that deals with IO streams is stdio.h in C or iostream in C++.

## Slide 177: Common functions for basic IO facilities
int getchar(void) -- reads a char from stdin
int putchar(char ch) -- writes a char to stdout, returns character written.
Related Functions:
int getc(FILE* stream); int putc(char ch, FILE* stream);
Notes:
At the first time the program needs input, OS stops the run and prompts user with blinking cursor.
User types input and presses ENTER. Only after it presses ENTER, all the typed data is written to the defined stream, and program continues running.
Now the program reads from the buffer as much as data as it needs. If user typed more than needed at the last read request, the rest of the data remains in the buffer for future stdin calls.
EOF - End Of File –defined at stdio.h: #define EOF -1
Ctrl +z = = artificial EOF

## Slide 178: scanf() : a wise input command
int scanf(char* format, args....)
Reads data from stdin and stores them according to the parameter format into
the locations pointed by the additional arguments.
The additional arguments should point to already allocated objects of the type specified by their corresponding format tag within the format string.
Example:
scanf("%7d%s %c% lf",&a, str, &ch, &x);
The above format string scans the first seven characters as a decimal integer, then reads the remaining as a string until a space, new line or tab is found, then scans the first non-whitespace character following and a double-precision floating-point number afterwards.
More at: http://www.cplusplus.com/reference/clibrary/cstdio/scanf/
** sscanf_examp.cpp

## Slide 179: scanf() : Related Functions
int sscanf ( const char * str, const char * format, ...);
similar to scanf() except that data is read from a string: str.
int fscanf ( FILE* stream, const char* format, ... );
Similar to scanf() but reads formatted data from a stream not necessarily stdin.

## Slide 180: printf() : a wise output command
int printf ( const char* format, ... );
Writes to the standard output (stdout) a sequence of data formatted as the format argument specifies.
After the format parameter, the function expects at least as many additional arguments as specified in format.
Example:
printf("Color %s, number1 %d, number2 %05d, hex %x, float %5.2f, unsigned value %u.\n",
"red",
123456,
89,
255,
3.14159,
250);
//output:
Color red, number1 123456, number2 00089, hex ff, float 3.14, unsigned value 250.

## Slide 181: Printf() - Related Functions:
int sprintf ( char* str, const char* format, ... );
similar to printf() except that data is written to a string: str.
int fprintf ( FILE* stream, const char* format, ... );
Write formatted output to a stream not necessarily stdout.
** sprintf_examp.cpp

## Slide 182: Getting and Putting an entire line at "one shot"
char* gets ( char* str );
Reads characters from stdin and stores them as a string into str until a newline character ('\n') or the End-of-File is reached.
int puts ( const char* str );
Writes the C string pointed by str to stdout and appends a newline character ('\n').
Caution note:
gets( ) might write to str more than it is allowed: must be careful with the size of the array pointed by str to avoid buffer overflows!
Low level IO – writing raw data bytes: each read/write request results in accessing disk (or device) directly to fetch/put a specific number of bytes. Data in this form is not buffered
** gets_examp.cpp

## Slide 183
the extern Keyword

## Slide 184: Extern keyword (1)
External variables are variables at file scope. They are defined outside the function and used inside it.
extern declares a reference to a variable defined elsewhere.
Once you have declared a reference to the variable at the external level, the variable is
visible throughout the remainder of the translation unit in which the declared reference occurs.
For an extern reference to be valid, the variable it refers to must be defined once, and
only once, at the external level. This definition can be in any of the translation units that make up the program.

## Slide 185: Extern keyword (2)
The extern keyword declares a variable or function and specifies that it has external
linkage (its name is visible from files other than the one in which it's defined).
When modifying a variable, extern specifies that the variable has static duration (it is
allocated when the program begins and de-allocated when the program ends).
The variable or function may be defined in another source file, or later in the same file. Declarations of variables and functions at file scope are external by default.
a function prototype using extern is only optional (i.e. default), since functions
can only be defined at the external level and cannot be nested. This means they
have "external linkage" by default. (Functions from other files are "known" to the
compiler when including their header files, signaling the compiler they would be linked later on).
Lesson 3 -extern

## Slide 186: Extern keyword (3)
Behind the scenes :
  a symbol table is a data structure used by the compiler, holding information about each identifier in the program's source code . That info can be its type, scope level and sometimes its location.
  An object file will contain a symbol table of the identifiers it contains that are externally visible. During the linking of different object files, a linker will use these symbol tables to resolve any unresolved references.
  extern tells the compiler that the variable will be found in the symbol table of a different translation unit.
  The external declaration is not resolved by the compiler, but instead by the linker: modularity at the compiler level.

## Slide 187
Static Variables

## Slide 188: Static Variables (1)
A static variable is a variable that has been allocated statically and whose lifetime extends across the entire run of the program.
Generally, static is a special type of local variable, called a static local, which:
is local to particular function (Outside the function can’t be accessed.)
is only initialized once (on the first call to function).
On the next call to the function, the static variable has the same value as on leaving.
* In this case of recursive calls to the function, it also has access to the single, statically allocated variable.
*If the function is global, the static variable declared in it is as a global variable in terms of space scope, except that its scope is only within that function.

## Slide 189: Static Variables (2)
Example 1:
int running_total()
{ static int sum = 0; sum ++; return sum;
}

## Slide 190: Static Variables (3)
Example 2:
void foo(void)
{ static int first=1; /* first is true */
if (first)
{ ... /* do something */
first = 0; /* now set it to false */
}
else
{
... /* do something else */
}
}

## Slide 191: Static Variables (4)
Notes:
Automatic variables are initialized during the run time. Static variables are initialized during the compile-time, so the initial values will simply be embedded in the executable file itself.
If you change them, they will retain changed in the file.

## Slide 192: Conclusion:
space scope | time scope/storage class | variable type
block | automatic | local
block | static | static local
current translation object | static | global
current or other translation objects of the program | static | Extern
depends on use | dynamic allocation | malloc()/realloc()

## Slide 193: More Variables
Storage duration specifiers :
  auto – by default for any local variable, so rarely used…
  register - hint to the compiler to cache the variable in a processor register. Other than not allowing the referencing operator (&) to be used on the variable or any of its subcomponents, the compiler is free to ignore the hint. (Microsoft compiler ignores this accept, and uses it just for debugging & requests)
  volatile -used to declare that an object that might be modified outside the program by the operating system or the hardware or a concurrently executing thread.
  The system always reads (from RAM) the current value of a volatile object at the point it is requested, even if a previous instruction asked for a value from the same object. Also, the value of the object is written (to RAM) immediately on assignment - volatile signal to the compiler not to optimize use of the variable that is declared.

## Slide 194
Linked Lists

## Slide 195
Singly Linked list
A linked list is a chain of structures which contain a pointer to the next element.
There are 3 main types of linked lists
Singly linked
Doubly linked
Trees
In a singly linked list, each node points forward to the next one, but not backward. Each Node includes:
the Data (int /structure/class)
the next Node
struct Node
{
int elem;
struct Node * next;
};
Head
Tail
next
next
next
next (null)

## Slide 196
Add(Node *list, Elem new)
{
  Node *newNode;
  newNode = (Node *) malloc (sizeof (Node));
  newNode -> elem = new;
  newNode -> next = list -> next;
  list -> next = newNode;
}
Remove(Node *list)
{
Node *temp = list -> next;
list -> next = temp -> next;
free (temp);
}
Adding and removing an element in the middle of the linked list is simple and fast.
Singly Linked list
196
next
next
next
next
next
next
next
next (null)
next (null)

## Slide 197
Linked list VS Array
Array | Linked List | 
O(1) | O(n) * | Indexing
Not Available | O(1) | Insert & Delete (in head / tail)
Not Available | SearchTime + Insert: O(n) + O(1) | Insert & Delete (in the middle)
0 Yet, fixed in size | (Node-Elem / Node) * N | Overhead
* The amount of time to be indexed can be shorten by a hash table, which will be explained in depth on the following pages.
197

## Slide 198
Doubly Linked list
**queue
**linked_list
A doubly linked list enables you to move backward and forward in the chain.
struct Node
{
int Elem;
struct Node * next1;
struct Node * prev;
};
Head
Tail
prev (null)
prev
prev
prev
Doubly
next (null)
next
next
next

## Slide 199
Using Stacks & Queues
The abstract concept of stacks and queues does not require a specific data structure, there is no restriction of some sort.
However, in most cases, it is recommended to implement both with linked list.
Stacks and Queues must implement the two functions:
  void push(element X)
  element X pop()
The terms used relating to stacks and queues are also FIFO and LIFO
199

## Slide 200
Binary Tree
A tree is a complex structure built from nodes, each of which can point in two or three directions
struct Node
{
  int Elem;
  struct Node * Left;
  struct Node *Right;
};
.
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem
left
right
Elem

## Slide 201
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
Advanced Tree Concepts
A numerical tree is a complex structure built from two special nodes, Left Child and Right Sibling.
struct Node
{
  int Elem;
  struct Node *LeftC;
  struct Node *RightS;
};
.
201
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem
child
sibling
Elem

## Slide 202
Hash Tables

## Slide 203
Hash Tables
The hash table or hash map is a data structure that uses a hash function to efficiently map certain identifiers or keys (e.g., person names) to associated values (e.g., their telephone numbers).
The hash function is used to transform the key into the index (the hash) of an array element (the slot or bucket) where the corresponding value is to be found.
Index = func (Key)

## Slide 204
Hash Tables
Ideally the hash function should map each possible key to a different slot index, but this is rarely achievable.
in practice Most hash table designs assume that hash collisions — pairs of different keys with the same hash values are normal occurrences and must be accommodated in some way
Head[0]
Head[1]
Head[2]
Head[3]
index

## Slide 205
Hash Function example
We have an pool of numbers all between 1-100 which we want to be able to access in approximately O(1).
Index = Hash_Function (Number) => Index = Number % 10
0
1
2
index
8
9
.
.
.
.
10
30
100
21
61
38
78
88

## Slide 206
Sorting Methods
Copyright @ 2007 Real Time College
206

## Slide 207
Bubble sort
It is the simplest sorting algorithm. The idea is to pass through the list checking for the right order by comparing two adjacent items.
Each comparison results in smaller on the left, bigger on the right. Swap as needed.
After each iteration the biggest item will bubble up, thus each iteration of passing through the array will be smaller by 1, until the array is sorted.
Processing N-1 iterations:
  ( 5 6 3 7 2 8 1 4 ) starting point
  ( 5 3 6 2 7 1 4 8 ) 8 bubbled up
  ( 3 5 2 6 1 4 7 8 ) 7 bubbled up
  ( 3 2 5 1 4 6 7 8 ) 6 bubbled up
  ( 2 3 1 4 5 6 7 8 ) 5 bubbled up
  ( 2 1 3 4 5 6 7 8 ) 4 bubbled up
  ( 1 2 3 4 5 6 7 8 ) 3 bubbled up
  ( 1 2 3 4 5 6 7 8 ) 2 bubbled up
Single iteration explanation:
  ( 5 6 3 7 2 8 1 4 ) 5<6 ok
  ( 5 6 3 7 2 8 1 4 ) 6>3 swap
  ( 5 3 6 7 2 8 1 4 ) 6<7 ok
  ( 5 3 6 7 2 8 1 4 ) 7>2 swap
  ( 5 3 6 2 7 8 1 4 ) 7<8 ok
  ( 5 3 6 2 7 8 1 4 ) 8>1 swap
  ( 5 3 6 2 7 1 8 4 ) 8>4 swap
  ( 5 3 6 2 7 1 4 8 ) 8 bubbled up

## Slide 208
Insertion sort
It is a simple algorithm. Here, sorting takes place by inserting a particular item at the appropriate position.
In general, in every iteration an item is compared with all the items before it, when the suitable position is found the items whose bigger are shifted forward.
In each iteration one more item is inserted, the process is repeated for all items, until the list is sorted.
Single iteration explanation:
  ( 5 6 3 7 2 8 1 4 ) 6 is in place
  ( 5 6 3 7 2 8 1 4 ) 3 is processed
  ( 5 3 6 7 2 8 1 4 ) 3 is processed
  ( 3 5 6 7 2 8 1 4 ) 3 is in place
  ( 5 3 6 7 2 8 1 4 ) 7 is in place
Processing N-1 iterations:
  ( 5 6 3 7 2 8 1 4 ) 6 is inserted
  ( 3 5 6 7 2 8 1 4 ) 3 is inserted
  ( 3 5 6 7 2 8 1 4 ) 7 is inserted
  ( 2 3 5 6 7 8 1 4 ) 2 is inserted
  ( 2 3 5 6 7 8 1 4 ) 8 is inserted
  ( 1 2 3 5 6 7 8 4 ) 1 is inserted
  ( 1 2 3 4 5 6 7 8 ) 4 is inserted
  ( 1 2 3 4 5 6 7 8 ) sorted

## Slide 209
Selection sort
Yet, another simple algorithm, somewhat similar to Insertion sort.
The list is again devided into the sorted area and the unsorted area. Each iteration, the next lowest item is beeing selected, and swapped to the correct position.
In each iteration the selected item is added to the sorted list, the process is repeated for all items, until the list is sorted.
Single iteration explanation:
  ( 5 6 3 7 2 8 1 4 ) 1 is selected
  ( 1 6 3 7 2 8 5 4 ) swapping [1 | 5]
  ( 1 6 3 7 2 8 5 4 ) 2 is selected
  ( 1 2 3 7 6 8 5 4 ) swapping [2 | 6]
  ( 1 2 3 7 6 8 5 4 ) 3 is selected
  ( 1 2 3 7 6 8 5 4 ) swapping [3 | 3]
Processing N-1 iterations:
  ( 5 6 3 7 2 8 1 4 ) 1 is selected
  ( 1 6 3 7 2 8 5 4 ) 2 is selected
  ( 1 2 3 7 6 8 5 4 ) 3 is selected
  ( 1 2 3 7 6 8 5 4 ) 4 is selected
  ( 1 2 3 4 6 8 5 7 ) 5 is selected
  ( 1 2 3 4 5 8 6 7 ) 6 is selected
  ( 1 2 3 4 5 6 7 8 ) 7 is selected
  ( 1 2 3 4 5 6 7 8 ) sorted

## Slide 210
Worst case performance | O(n2)
Best case performance | O(n)
Average case performance | O(n2)
Worst case performance | О(n2)
Best case performance | О(n2)
Average case performance | О(n2)
Bubble Sort
Selection Sort
Worst case performance | О(n2)
Best case performance | O(n)
Average case performance | О(n2)
Insertion Sort
Comparison

## Slide 211
Shell sort
An expansion of Insertion and Bubble sort. Done by partially sorting items with a shrinking gap. The sorting can be very efficient on a large set of items.
Sorting is done several times, on sub-arrays of the main array. Each sub array is a group of items that lie far apart. Example – items:[0,8,16,24] items:[1,9,17,25] ..
The running time of Shellsort is heavily dependent on the gap sequence it uses.
Sorting explanation: Gap=4.
  ( 5 6 3 7 2 8 1 4 ) 1st group
  ( 5 6 3 7 2 8 1 4 ) 2nd group
  ( 5 6 3 7 2 8 1 4 ) 3rd group
  ( 5 6 3 7 2 8 1 4 ) 4th group
  ( 2 6 1 4 5 8 3 7 ) partially sorted.
Sorting explanation: Gap=3.
  ( 2 6 1 4 5 8 3 7 ) 1st group
  ( 2 6 1 4 5 8 3 7 ) 2nd group
  ( 2 6 1 4 5 8 3 7 ) 3rd group
  ( 2 5 1 3 6 8 4 7 ) partially sorted.
Sorting explanation: Gap=1.
  ( 2 5 1 3 6 8 4 7 ) regular sorting
  ( 1 2 3 4 5 6 7 8 ) sorted

## Slide 212
Worst case performance | depends on gap sequence
Best case performance | O(N)
Average case performance | depends on gap sequence
Worst case space complexity | O(1)
Shell sort performance

## Slide 213
Merge sort
A sophisticated divide and conquer algorithm that uses two basic functions to operate. merge-sort to split, and merge to sort. Splitting is done recursively.
The splitting is done recursively with merge-sort until the size of the array is 1.
The merging is done backwards. It takes two already sorted sub-arrays and merges them
First thing, understanding merge:
Lets assume we have two sorted sub-ararys:
    ( 1 6 8 15 24 30 ) sub-array 1 ( 2 5 9 14 20 32 ) sub-array 2
The next thing to do is to build a single sorted array which combines all items:
    ( 1 6 8 15 24 30 ) sub-array 1 ( 2 5 9 14 20 32 ) sub-array 2
    Item 1<2, choosing 1 ( 1 )
    ( 1 6 8 15 24 30 ) sub-array 1 ( 2 5 9 14 20 32 ) sub-array 2
    Item 6>2, choosing 2 ( 1 2 )
    ( 1 6 8 15 24 30 ) sub-array 1 ( 2 5 9 14 20 32 ) sub-array 2
    Item 6>5, choosing 5 ( 1 2 5 )
    ( 1 6 8 15 24 30 ) sub-array 1 ( 2 5 9 14 20 32 ) sub-array 2
213

## Slide 214
Merge sort (2)
Understanding merge:
  ( 1 6 8 15 24 30 ) sub-array 1 ( 2 5 9 14 20 32 ) sub-array 2
    Item 6<9, choosing 6 ( 1 2 5 6 )
    Item 8<9, choosing 8 ( 1 2 5 6 8 )
    Item 15>9, choosing 9 ( 1 2 5 6 8 9 )
    Item 15>14, choosing 14 ( 1 2 5 6 8 9 14 ) and so on …
Understanding merge_sort:
    Lets assume we have unsorted array. Lets define left, rigt and middle, in order to split.
23
13
6
72
24
15
40
38
9
10
62
99
31
56
Left
Right
Middle
Middle+1
23
13
6
72
24
15
40
38
9
10
62
99
31
56
Left
Right
Left
Right
Middle
Middle+1
23
13
6
Left
Right
23
13
6
72
24
15
40
Left
Right
Left
Right
214

## Slide 215
Understanding merge_sort:
    Ultimately after splitting and merging the list will be sorted.
23
13
6
72
24
15
40
38
9
10
62
99
31
56
23
13
6
72
24
15
40
38
9
10
62
99
31
56
23
13
6
23
13
6
72
24
15
40
72
24
15
40
38
9
10
62
99
31
56
9
10
38
62
99
31
56
56
31
99
62
9
10
38
40
15
24
72
6
13
23
23
6
13
24
72
15
40
9
10
38
62
99
31
56
6
13
23
15
24
40
72
9
10
38
31
56
62
99
6
13
15
23
24
40
72
9
10
31
38
56
62
99
6
9
10
13
15
23
24
31
38
40
56
62
72
99
Merge sort (3)
Splitting
Merging
215

## Slide 216
Merge sort performance
Worst case performance | O(n log n)
Best case performance | O(n log n) typical, O(n) natural variant
Average case performance | O(n log n)
Worst case space complexity | O(n) auxiliary
Parallel processing:
Merge sort can be multi processed well due to use of divide-and-conquer method.
The multi processing can be done not only on the recursive division of the array, but also the merge operation.
216

## Slide 217
Binary Tree sort
23
13
6
72
24
15
40
38
9
10
62
99
31
56
A tree sort is a sort algorithm that builds a binary search tree from the items to be sorted, and then traverses the tree (in-order) so that the items come out in sorted order.
Both the insertion and the removal is done recursively.
Its typical use is when sorting the elements of a stream from a file.
23
13
6
15
72
24
99
40
null
38
62
null
null
9
10
null
31
null
56
null
null
null
null
null
null
null
null
null
null
6
9
10
13
15
23
24
31
38
40
56
62
72
99
217

## Slide 218
Worst case performance | O(n2) (unbalanced) O(n log n) (balanced)
Best case performance | O(n)
Average case performance | O(n log n)
Binary Tree sort performance
218

## Slide 219
Heap sort
23
13
6
72
24
15
40
38
9
10
62
99
31
56
Heap sort is a much more efficient version of selection sort.
It works by constructing a special data structure called heap, similar to Binary Tree sorting.
The primary rule is that no child is bigger then it’s father. Swap as needed. There are two parts, creating a Heapified list, and creating the sorted list. Please follow the example:
23
13
6
72
72
23
6
13
24
15
40
38
9
10
62
99
31
56
72
23
6
13
72
24
6
13
23
15
40
38
9
10
62
99
31
56
72
23
6
24
13
15
72
24
15
13
23
6
40
38
9
10
62
99
31
56
72
24
15
23
13
6
72
24
15
23
13
40
6
72
24
40
13
23
6
15
38
9
10
62
99
31
56
72
24
40
23
13
15
6
38
72
38
40
24
23
6
15
13
9
10
62
99
31
56
(1.0)
(1.1)
(1.2)
(1.3)
(1.0-1.1)
(1.1)
(1.4)
(1.5)
(1.2-1.3)
(1.3)
(1.4)
(1.5)
219

## Slide 220
Heapified:
Heap sort (2)
72
38
40
23
24
15
6
9
13
62
10
72
38
40
24
23
6
15
13
9
10
62
99
31
56
72
62
40
24
38
6
15
13
9
10
23
99
31
56
72
62
40
38
24
15
6
9
13
23
10
99
99
62
72
38
24
15
40
9
13
23
10
31
6
56
99
62
72
38
24
56
40
9
13
23
10
31
6
15
99
62
72
24
38
40
15
13
9
10
23
6
31
56
99
62
72
24
38
40
56
13
9
10
23
6
31
15
99
62
72
24
38
40
56
13
9
10
23
6
31
15
(2.0)
(2.1)
(2.2)
(2.3)
(2.1)
(2.2)
(2.3)
220
220

## Slide 221
The array is beeing divided to the heaped
part (left) and the sorted part (right).
The biggest (first of the heap) is moved right.
99
62
72
38
24
56
40
9
13
23
10
31
6
15
15
62
72
38
24
56
40
9
13
23
10
31
6
99
62
72
24
38
40
56
13
9
10
23
6
31
15
The array is not sorted yet. The biggest item
Though, must be the first.
15
62
72
24
38
40
56
13
9
10
23
6
31
99
72
62
56
38
24
15
40
9
13
23
10
31
6
After the swap we rearrange our heap.
Swapping downwards with the biggest child.
15
62
72
24
38
40
56
13
9
10
23
6
31
99
72
62
56
24
38
40
15
13
9
10
23
6
31
99
Heap sort (3)
221

## Slide 222
72
62
56
38
24
15
40
9
13
23
10
31
6
72
62
56
24
38
40
15
13
9
10
23
6
31
99
31
62
56
38
24
15
40
9
13
23
10
6
31
62
56
24
38
40
15
13
9
10
23
6
72
99
62
38
56
31
24
15
40
9
13
23
10
6
62
38
56
24
31
40
15
13
9
10
23
6
72
99
6
38
56
31
24
15
40
9
13
23
10
6
38
56
24
31
40
15
13
9
10
23
62
72
99
Heap sort (4)
(3.1)
(3.2)
(3.3)
(3.4)
222

## Slide 223
56
38
40
31
24
6
9
13
23
10
15
56
38
40
24
31
6
15
13
9
10
23
62
72
99
23
38
40
31
24
6
9
13
10
15
40
38
23
31
24
6
9
13
10
15
40
38
23
24
31
6
15
13
9
10
56
62
72
99
40
38
23
31
24
6
9
13
10
15
40
38
23
24
31
6
15
13
9
10
56
62
72
99
10
38
23
31
24
6
9
13
15
38
31
10
24
15
9
13
23
6
38
31
23
24
10
6
15
13
9
40
56
62
72
99
38
31
23
24
10
6
15
13
9
40
56
62
72
99
31
24
23
13
10
6
15
9
38
40
56
62
72
99
38
31
10
24
15
9
13
23
6
9
31
10
24
15
13
23
6
31
24
10
13
15
9
23
6
Heap sort (5)
(4.1.1)
(4.1.2)
(4.1.3)
(4.2.1)
(4.2.2)
(4.2.3)
(4.3.1)
(4.3.1)
(4.3.3)
223

## Slide 224
31
24
10
13
15
9
23
6
9
24
10
13
15
23
6
24
13
10
9
15
23
6
15
24
10
13
23
6
31
24
23
13
10
6
15
9
38
40
56
62
72
99
9
24
23
13
10
6
15
31
38
40
56
62
72
99
24
13
23
9
10
6
15
13
23
9
10
6
15
31
38
..
31
38
..
24
Heap sort (6)
As we go on, the heaped part of the array is getting smaller,
and the sorted part is getting Bigger.
The operation continues until the heaped part is gone and the array is sorted.
224

## Slide 225
Worst case performance | O(n log n)
Best case performance | Ω(n),O(n log n)[1]
Average case performance | O(n log n)
Worst case space complexity | O(n) total, O(1)auxiliary
Heap sort performance
225

## Slide 226
Quick sort
3
7
8
5
2
1
9
5
4
Quicksort is a divide and conquer algorithm.
It first divides a large list into two smaller sub-lists: the low elements and the high elements. Then it continues the operation for each sub-list.
The transition of sorting the sub-lists is usually done recursively.
3
4
2
1
5
5
9
8
7
Smaller
Bigger or equal
226

## Slide 227
Quick sort
Single iteration explanation:
  ( 3 7 8 5 2 1 9 4 ) 5 is selected
  working on 5
  ( 3 7 8 4 2 1 9 5 ) 7 > 5 and 1 <= 5
  ( 3 1 8 4 2 7 9 5 ) swapped! next ..
  ( 3 1 8 4 2 7 9 5 ) 8 > 5 and 2 <= 5
  ( 3 1 2 4 8 7 9 5 ) time to end iter’
  ( 3 1 2 4 5 7 9 8 ) 5 in place …
Processing next iterations:
( 3 1 2 4 ) ( 5 7 9 8 ) doing the same for each
Basically it’s time to practice ..
( _ _ _ _ ) ( _ _ _ _ )
( _ _ _ _ ) ( _ _ _ _ )
( _ _ _ _ ) ( _ _ _ _ )
( _ _ _ _ ) ( _ _ _ _ )
( _ _ _ _ ) ( _ _ _ _ )
( _ _ _ _ ) ( _ _ _ _ )
( _ _ _ _ ) ( _ _ _ _ )
5
Smaller
Bigger

## Slide 228
Worst case performance | O(n2)
Best case performance | O(n log n)
Average case performance | O(n log n)
Worst case space complexity | O(n)
Parallelization:
Like merge sort, quicksort can also be parallelized due to its divide-and-conquer nature.
Individual in-place partition operations are difficult to parallelize, but once divided, different sections of the list can be sorted in parallel.
If we have (p) processors, we can divide a list of n elements into p sub-lists in O(n) average time, then sort each of these in average time.
Quick sort performance
228